## Slide 1
Chapter 4
Data-Level Parallelism in Vector, SIMD, and GPU Architectures
Computer Architecture
A Quantitative Approach, Fifth Edition

## Slide 2: Flynn’ taxonomy
Single instruction stream single data stream (SISD)
Single instruction stream, multiple data streams (SIMD)
  Vector processor, Multimedia extensions on modern processors
Multiple instruction streams, single data stream (MISD)
  Stream processors (somewhat…)
  Exotic fault tolerance architectures (eg Space Shuttle)
Multiple instruction streams, multiple data streams (MIMD)
  Multi-core systems
  Multi-processor systems
  Distributed systems

## Slide 3: Introduction
SIMD architectures can exploit significant data-level parallelism for:
  matrix-oriented scientific computing
  media-oriented image and sound processors
SIMD allows programmer to continue to think sequentially
Introduction

## Slide 4: VECTOR ARCHITECTURES

## Slide 5: Vector Architectures
Basic idea:
  Read sets of data elements into “vector registers”
  Operate on those registers
  Disperse the results back into memory
Registers are controlled by compiler
  Used to hide memory latency
  Leverage memory bandwidth
Vector Architectures

## Slide 6: VMIPS
Example (fictional) architecture: VMIPS
  Loosely based on Cray-1
  Vector registers
    Each register holds a 64-element, 64 bits/element vector
    Register file has 16 read ports and 8 write ports
  Vector functional units
    Fully pipelined
    Data and control hazards are detected
  Vector load-store unit
    Fully pipelined
    One word per clock cycle after initial latency
  Scalar registers
    32 general-purpose registers
    32 floating-point registers
Vector Architectures

## Slide 7: VMIPS Instructions
ADDVV.D: add two vectors
ADDVS.D: add vector to a scalar
LV/SV: vector load and vector store from address
Example: DAXPY (Y = a * X + Y)
  L.D F0,a ; load scalar a
  LV V1,Rx ; load vector X
  MULVS.D V2,V1,F0 ; vector-scalar multiply
  LV V3,Ry ; load vector Y
  ADDVV V4,V2,V3 ; add
  SV Ry,V4 ; store the result
Requires 6 instructions vs. almost 600 for MIPS
Vector Architectures

## Slide 8: Instructions (p. 266)
ADDVV.D V1,V2,V3
ADDVS.D V1,V2,F0
SUBVV.D V1,V2,V3
SUBVS.D V1,V2,F0
SUBSV.D V1,F0,V3
MULVV.D V1,V2,V3
DIVVV.D V1,V2,V3
LV V1,R1
SV R1,V1
LVWS V1,(R1,R2) Load w/ stride (R1+i*R2)
S--VV.D V1,V2 Compare elements (EQ, NE,GT…)
S--VS.D V1,F0 and set vector mask register (VM)

## Slide 9: Vector Execution Time
Execution time depends on three factors:
  Length of operand vectors
  Structural hazards
  Data dependencies
VMIPS functional units consume one element per clock cycle
  Execution time is approximately the vector length
Vector Architectures

## Slide 10: Challenges
Start up time
  Latency of vector functional unit
  Assume the same as Cray-1
    Floating-point add => 6 clock cycles
    Floating-point multiply => 7 clock cycles
    Floating-point divide => 20 clock cycles
    Vector load => 12 clock cycles
Improvements:
  > 1 element per clock cycle
  Non-64 wide vectors
  IF statements in vector code
  Memory system optimizations to support vector processors
  Multiple dimensional matrices
  Sparse matrices
  Programming a vector computer
Vector Architectures

## Slide 11: Multiple Lanes
Element n of vector register A is “hardwired” to element n of vector register B
  Allows for multiple hardware lanes
Vector Architectures

## Slide 12: Vector Length Register
Vector length not known at compile time?
Use Vector Length Register (VLR)
Use strip mining for vectors over the maximum length:
  low = 0;
  VL = (n % MVL); /*find odd-size piece using modulo op % */
  for (j = 0; j <= (n/MVL); j=j+1) { /*outer loop*/
  for (i = low; i < (low+VL); i=i+1) /*runs for length VL*/
  Y[i] = a * X[i] + Y[i] ; /*main operation*/
  low = low + VL; /*start of next vector*/
  VL = MVL; /*reset the length to maximum vector length*/
  }
Vector Architectures

## Slide 13: Vector Mask Registers
Consider:
for (i = 0; i < 64; i=i+1)
if (X[i] != 0)
X[i] = X[i] – Y[i];
Use vector mask register to “disable” elements:
LV V1,Rx ;load vector X into V1
LV V2,Ry ;load vector Y
L.D F0,#0 ;load FP zero into F0
SNEVS.D V1,F0 ;sets VM(i) to 1 if V1(i)!=F0
SUBVV.D V1,V1,V2 ;subtract under vector mask
SV Rx,V1 ;store the result in X
GFLOPS rate decreases!
Vector Architectures

## Slide 14: Memory Banks
Memory system must be designed to support high bandwidth for vector loads and stores
Spread accesses across multiple banks
  Control bank addresses independently
  Load or store non sequential words
  Support multiple vector processors sharing the same memory
Example:
  32 processors, each generating 4 loads and 2 stores/cycle
  Processor cycle time is 2.167 ns, SRAM cycle time is 15 ns
  How many memory banks needed?
Vector Architectures

## Slide 15: Stride: handling multidimensional arrays
Consider:
for (i = 0; i < 100; i=i+1)
for (j = 0; j < 100; j=j+1) {
A[i][j] = 0.0;
for (k = 0; k < 100; k=k+1)
A[i][j] = A[i][j] + B[i][k] * D[k][j];
}
Must vectorize multiplication of rows of B with columns of D
Use non-unit stride
  Loading: load non-consecutive memory locations in consecutive vector register locations
  Saving…
  Complicates the memory system
Vector Architectures

## Slide 16: Scatter-Gather: handling sparse matrices
In sparse matrices, the elements of the vector are stored in some compacted form and accessed indirectly.
Consider:
for (i = 0; i < n; i=i+1)
A[K[i]] = A[K[i]] + C[M[i]];
Use index vector which indicates the non-zero elements of the vector, and allows to load them
LV Vk, Rk ;load K
LVI Va, (Ra+Vk) ;load A[K[]]
LV Vm, Rm ;load M
LVI Vc, (Rc+Vm) ;load C[M[]]
ADDVV.D Va, Va, Vc ;add them
SVI (Ra+Vk), Va ;store A[K[]]
Vector Architectures

## Slide 17: sIMD EXTENSIONS

## Slide 18: SIMD Extensions
Media applications operate on data types narrower than the native word size
  Example: disconnect carry chains to “partition” adder
Limitations, compared to vector instructions:
  Number of data operands encoded into op code
  No sophisticated addressing modes (strided, scatter-gather)
  No mask registers
SIMD Instruction Set Extensions for Multimedia

## Slide 19: SIMD Implementations
Implementations:
  Intel MMX (1996)
    Eight 8-bit integer ops or four 16-bit integer ops
  Streaming SIMD Extensions (SSE) (1999)
    Eight 16-bit integer ops
    Four 32-bit integer/fp ops or two 64-bit integer/fp ops
  Advanced Vector Extensions (2010)
    Four 64-bit integer/fp ops
  Operands must be consecutive and aligned memory locations
SIMD Instruction Set Extensions for Multimedia

## Slide 20: SIMD extensions today (Fall 2017)
Latest iteration of SIMD extensions – AVX-512
  Available in Intel i9 series
Intel AVX-512 features include 32 vector registers each 512 bits wide, eight dedicated mask registers, 512-bit operations on packed floating point data or packed integer data, embedded rounding controls (override global settings), embedded broadcast, embedded floating-point fault suppression, embedded memory fault suppression, new operations, additional gather/scatter support, high speed math instructions, compact representation of large displacement value, and the ability to have optional capabilities beyond the foundational capabilities. It is interesting to note that the 32 ZMM registers represent 2K of register space!