## Slide 1
Chapter 2
Memory Hierarchy Design
Computer Architecture
A Quantitative Approach, Fifth Edition

## Slide 2: Memory Hierarchy
Introduction

## Slide 3: Causes of misses
Compulsory
  First reference to a block
Capacity
  Blocks discarded and later retrieved
Conflict
  Program makes repeated references to multiple addresses from different blocks that map to the same location in the cache
Introduction

## Slide 4: Memory Hierarchy Basics
Note that speculative and multithreaded processors may execute other instructions during a miss
  Reduces performance impact of misses
Introduction

## Slide 5: Memory Hierarchy Basics
Six basic cache optimizations:
  Larger block size
    Reduces compulsory misses
    Increases capacity and conflict misses, increases miss penalty
  Larger total cache capacity to reduce miss rate
    Increases hit time, increases power consumption
  Higher associativity
    Reduces conflict misses
    Increases hit time, increases power consumption
  Higher number of cache levels
    Reduces overall memory access time
  Giving priority to read misses over writes
    Use a write buffer!
    Reduces miss penalty
  Avoiding address translation in cache indexing
    Reduces hit time
Introduction

## Slide 6: Advanced cache optimizations

## Slide 7: 1. Small and simple first level caches
Critical timing path:
  addressing tag memory, then
  comparing tags, then
  selecting correct set
Direct-mapped caches can overlap tag compare and transmission of data
Lower associativity reduces power because fewer cache lines are accessed
Advanced Optimizations

## Slide 8: 2. Way Prediction
To improve hit time, predict the way to pre-set mux
  Mis-prediction gives longer hit time
  Prediction accuracy
    > 90% for two-way
    > 80% for four-way
    I-cache has better accuracy than D-cache
  First used on MIPS R10000 in mid-90s
  Used on ARM Cortex-A8
Extend to predict block as well
  “Way selection”
  Increases mis-prediction penalty
Advanced Optimizations

## Slide 9: 3. Pipelining Cache
Pipeline cache access to improve bandwidth
  Examples:
    Pentium: 1 cycle
    Pentium Pro – Pentium III: 2 cycles
    Pentium 4 – Core i7: 4 cycles
Increases branch mis-prediction penalty
Makes it easier to increase associativity
Advanced Optimizations

## Slide 10: 4. Nonblocking Caches
Allow hits before previous misses complete
  “Hit under miss”
  “Hit under multiple miss”
L2 must support this
In general, processors can hide L1 miss penalty but not L2 miss penalty
Advanced Optimizations

## Slide 11: 5. Multibanked Caches
Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
Interleave banks according to block address
Advanced Optimizations

## Slide 12: 6. Critical Word First, Early Restart
Critical word first
  Request missed word from memory first
  Send it to the processor as soon as it arrives
Early restart
  Request words in normal order
  Send missed work to the processor as soon as it arrives
Effectiveness of these strategies depends on block size and likelihood of another access to the portion of the block that has not yet been fetched
Advanced Optimizations

## Slide 13: 7. Merging Write Buffer
When storing to a block that is already pending in the write buffer, update write buffer
Reduces stalls due to full write buffer
Do not apply to I/O addresses
Advanced Optimizations
No write buffering
Write buffering

## Slide 14: 8. Compiler Optimizations
Loop Interchange
  Swap nested loops to access memory in sequential order
Blocking
  Instead of accessing entire rows or columns, subdivide matrices into blocks
  Requires more memory accesses but improves locality of accesses
Advanced Optimizations

## Slide 15: 9. Hardware Prefetching
Fetch two blocks on miss (include next sequential block)
Advanced Optimizations
Pentium 4 Pre-fetching

## Slide 16: 10. Compiler Prefetching
Insert prefetch instructions before data is needed
Non-faulting: prefetch doesn’t cause exceptions
Register prefetch
  Loads data into register
Cache prefetch
  Loads data into cache
Combine with loop unrolling and software pipelining
Advanced Optimizations

## Slide 17: Summary
Advanced Optimizations