## Slide 1: Chapter 1
Computer Abstractions and Technology

## Slide 2: Classes of Computers
Personal computers
  General purpose, variety of software
  Subject to cost/performance tradeoff
Server computers
  Network based
  High capacity, performance, reliability
  Range from small servers to building sized

## Slide 3: Classes of Computers
Supercomputers
  High-end scientific and engineering calculations
  Highest capability but represent a small fraction of the overall computer market
Embedded computers
  Hidden as components of systems
  Stringent power/performance/cost constraints

## Slide 4: The PostPC Era

## Slide 5: The PostPC Era
Personal Mobile Device (PMD)
  Battery operated
  Connects to the Internet
  Hundreds of dollars
  Smart phones, tablets, electronic glasses
Cloud computing
  Warehouse Scale Computers (WSC)
  Software as a Service (SaaS)
  Portion of software run on a PMD and a portion run in the Cloud
  Amazon AWS, Google Compute Engine, Microsoft Azure

## Slide 6: Computer HARDWARE and SOFTWARE

## Slide 7: Components of a Computer
Same components for all kinds of computer
  Desktop, server, embedded
Input/output includes
  User-interface devices
    Display, keyboard, mouse
  Storage devices
    Hard disk, CD/DVD, flash
  Network adapters
    For communicating with other computers
§1.4 Under the Covers
The BIG Picture

## Slide 8: Below Your Program
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers
§1.3 Below Your Program

## Slide 9: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 10: A Safe Place for Data
Volatile main memory
  Loses instructions and data when power off
Non-volatile secondary memory
  Magnetic disk
  Flash memory
  Optical disk (CDROM, DVD)

## Slide 11: Networks
Communication, resource sharing, nonlocal access
Local area network (LAN): Ethernet
Wide area network (WAN): the Internet
Wireless network: WiFi, Bluetooth

## Slide 12: Abstractions
Abstraction helps us deal with complexity
  Hide lower-level detail
Instruction set architecture (ISA)
  The hardware/software interface
Application binary interface
  The ISA plus system software interface
Implementation
  The details underlying and interface
The BIG Picture

## Slide 13: Integrated Circuit Cost
Nonlinear relation to area and defect rate
  Wafer cost and area are fixed
  Defect rate determined by manufacturing process
  Die area determined by architecture and circuit design

## Slide 14: Performance

## Slide 15: Defining Performance
Which airplane has the best performance?
§1.6 Performance

## Slide 16: Response Time and Throughput
Response time
  How long it takes to do a task
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll focus on response time for now…

## Slide 17: Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B

## Slide 18: Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance

## Slide 19: Measuring performance on benchmarks
Benchmark: agreed upon application, used for performance studies
Real application
  Most representative
  Most difficult to set up
Application kernels
  Find the most time consuming part of an app
Synthetic benchmarks
  Simplified kernels
  Useful for design studies
Peak performance
  Only useful in marketing slides

## Slide 20: Understanding Performance
Algorithm
  Determines number of operations executed
Programming language, compiler, architecture
  Determine the number of machine instructions executed per operation
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed

## Slide 21: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock (cycles)
Data transfer and computation
Update state
Clock period
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 22: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 23: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 24: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
A is faster…
…by this much

## Slide 25: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 26: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc
The BIG Picture

## Slide 27: Uniprocessor Performance
§1.8 The Sea Change: The Switch to Multiprocessors
Constrained by power, instruction-level parallelism, memory latency

## Slide 28: Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization

## Slide 29: Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
§1.10 Fallacies and Pitfalls
  Can’t be done!
Example: multiply accounts for 80s/100s
  How much improvement in multiply performance to get 5× overall?
Corollary: make the common case fast

## Slide 30: POWER CONSUMPTION

## Slide 31: Power Trends
In CMOS IC technology
§1.7 The Power Wall
×1000
×30
5V → 1V

## Slide 32: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 33: Eight Great Ideas
Design for Moore’s Law
Use abstraction to simplify design
Make the common case fast
Performance via parallelism
Performance via pipelining
Performance via prediction
Hierarchy of memories
Dependability via redundancy
§1.2 Eight Great Ideas in Computer Architecture

## Slide 34: Concluding Remarks
Cost/performance is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Instruction set architecture
  The hardware/software interface
Execution time: the best performance measure
Power is a limiting factor
  Use parallelism to improve performance
§1.9 Concluding Remarks