## Slide 1: What’s the Internet: “nuts and bolts” view
millions of connected computing devices: hosts = end systems
  running network apps
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
router
PC
server
wireless
laptop
cellular
handheld
wired
links
access
points
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth
routers: forward packets (chunks of data)

## Slide 2: What’s the Internet: “nuts and bolts” view
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, Ethernet
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
Home network
Institutional network
Mobile network
Global ISP
Regional ISP

## Slide 3: What’s the Internet: a service view
communication infrastructure enables distributed applications:
  Web, VoIP, email, games, e-commerce, file sharing
communication services provided to apps:
  reliable data delivery from source to destination
  “best effort” (unreliable) data delivery

## Slide 4: A closer look at network structure:
network edge: applications and hosts
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks

## Slide 5: The network edge:
end systems (hosts):
  run application programs
  e.g. Web, email
  at “edge of network”
client/server
peer-peer
client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
peer-peer model:
  minimal (or no) use of dedicated servers
  e.g. Skype, BitTorrent

## Slide 6: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 7: Ways to access the internet

## Slide 8: Dial-up Modem
telephone
network
Internet
home dial-up
modem
ISP modem
(e.g., AOL)
home
PC
central office
Uses existing telephony infrastructure
  Home is connected to central office
up to 56Kbps direct access to router (often less)
Can’t surf and phone at same time: not “always on”

## Slide 9: Digital Subscriber Line (DSL)
telephone
network
DSL
modem
home
PC
home
phone
Internet
DSLAM
Existing phone line: 0-4KHz phone; 4-50KHz upstream data; 50KHz-1MHz downstream data
splitter
central
office
  Also uses existing telephone infrastruture
  up to 1 Mbps upstream (today typically < 256 kbps)
  up to 8 Mbps downstream (today typically < 1 Mbps)
  dedicated physical line to telephone central office

## Slide 10: Residential access: cable modems
Does not use telephone infrastructure
  Instead uses cable TV infrastructure
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream, 2 Mbps upstream
network of cable and fiber attaches homes to ISP router
  homes share access to router
  unlike DSL, which has dedicated access

## Slide 11: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)
Typically 500 to 5,000 homes

## Slide 12: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)

## Slide 13: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
FDM (more shortly):

## Slide 14: Fiber to the Home
ONT
OLT
central office
optical
splitter
ONT
ONT
optical fiber
optical fibers
Internet
Optical links from central office to the home
Two competing optical technologies:
  Passive Optical network (PON) – unpowered optical splitters
  Active Optical Network (A0N) – rely on proper switching/routing
Much higher Internet rates; fiber also carries television and phone services
Example: Verizon FiOS, Google Fiber for Communities
ONT  optical network terminator
OLT  optical line terminator

## Slide 15: Fiber to the home examples
Verizon FiOS
  Passive Optical Network
  Highest tier: 150Mbit/s down and 35Mbit/s up for $199/month
Google Fiber to Communities
  1Gbit/s for a selected community
  1,100 communities applied
  Not yet announced who will get it (“early 2011”)

## Slide 16: Ethernet Internet access
100 Mbps
100 Mbps
100 Mbps
1 Gbps
server
Ethernet
switch
Institutional
router
To Institution’s ISP
Typically used in companies, universities, etc
  10 Mbs, 100Mbps, 1Gbps, 10Gbps Ethernet
  Today, end systems typically connect into Ethernet switch

## Slide 17: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  802.11b/g (WiFi): 11 or 54 Mbps
  802.11n: 600 Mbps
wider-area wireless access
  provided by telco operator
  3G: ~1Mbps over cellular system (EVDO – Verizon, Spring, HSPA+ AT&T, T-Mobile)
  4G:
    LTE (Sprint, Verizon)
    WiMAX (10’s Mbps) over wide area – higher frequencies: Clearwire, AT&T Alaska etc.
base
station
mobile
hosts
router