## Slide 1: Elements of a wireless network
network
infrastructure
wireless hosts
laptop, PDA, IP phone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility

## Slide 2: Elements of a wireless network
network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers 802.11 access points

## Slide 3: Elements of a wireless network
network
infrastructure
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance

## Slide 4: Characteristics of selected wireless link standards
384 Kbps
56 Kbps
54 Mbps
5-11 Mbps
1 Mbps
802.15
802.11b
802.11{a,g}
IS-95 CDMA, GSM
UMTS/WCDMA, CDMA2000
.11 p-to-p link
2G
3G
Indoor
10 – 30m
Outdoor
50 – 200m
Mid range
outdoor
200m – 4Km
Long range
outdoor
5Km – 20Km
New developments
802.11n, up to 4 antenas, up to 600Mbps, about 70m indoor, 250m outdoor range
LTE (100 down / 50 up Mbps)
WiMax (802.16) (128 down / 56 up Mbps)
Note: 802.15 is Bluetooth

## Slide 5: Elements of a wireless network
network
infrastructure
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network

## Slide 6: Elements of a wireless network
Ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 7: Wireless Link Characteristics
Differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
  multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 8: Wireless network characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal fading:
B, A hear each other
B, C hear each other
A, C can not hear each other interferring at B

## Slide 9: IEEE 802.11 Wireless LAN
802.11b
  2.4-5 GHz unlicensed radio spectrum
  up to 11 Mbps
  direct sequence spread spectrum (DSSS) in physical layer
    all hosts use same chipping code
  widely deployed, using base stations
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
All use CSMA/CA for multiple access
All have base-station and ad-hoc network versions

## Slide 10: 802.11n
Evolution of the 802.11a/g
Adds:
  Multiple input multiple output MIMO at the physical layer
  40 MHz channels (instead of 20MHz)
  Frame aggregation at the link layer (multiple Ethernet frames in a single transmission, reduces overhead)
Uses both the 2.5 and 5GHz unlicensed spectrum
Theoretical max: 600Mbps – with 4 MIMO channels.
Has been in the standardization process for 12 years (1997 – 2009), people got impatient (pre-N) devices.

## Slide 11: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch
or router
AP
AP

## Slide 12: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies; 3 non-overlapping
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with; initiates association protocol
  may perform authentication [Chapter 8]
  will typically run DHCP to get IP address in AP’s subnet

## Slide 13: IEEE 802.11: multiple access
Like Ethernet, uses CSMA:
  random access
  carrier sense: don’t collide with ongoing transmission
Unlike Ethernet:
  no collision detection – transmit all frames to completion
  acknowledgment – because without collision detection, you don’t know if your transmission collided or not
Why no collision detection?
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
Goal: avoid collisions: CSMA/C(ollision)A(voidance)

## Slide 14: Coordination of transmissions
Set of rules.
Standard allows a number of different behaviors
DCF – distributed coordinated function (see next slide)
  Exponential backoff with some specifics
PCF – point coordination function
  The access points has priority

## Slide 15: IEEE 802.11 MAC Protocol: CSMA/CA (in DCF mode)
802.11 sender
1 if sense channel idle for DIFS then
  - transmit entire frame (no CD)
2 if sense channel busy then
  - start random backoff time
  - timer counts down while channel idle
  - transmit when timer expires
  - if no ACK, increase random backoff interval, repeat 2
802.11 receiver
if frame received OK
- return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK

## Slide 16: RTS/CTS
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
optional; not typically used
sender first transmits small request-to-send (RTS) packets to AP using CSMA
  RTSs may still collide with each other (but they’re short)
AP broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
You can turn this on/off in your WiFi driver.
Avoid data frame collisions completely
using small reservation packets!

## Slide 17: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 18: 802.11 frame: addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 3: used only in ad hoc mode

## Slide 19
Internet
router
AP
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr AP MAC addr
dest. address
source address
802.3 frame
802.11 frame: addressing

## Slide 20
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
802.11 frame: more
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for reliable ARQ)
frame type
(RTS, CTS, ACK, data)

## Slide 21
hub or
switch
AP 2
AP 1
H1
BBS 2
BBS 1
802.11: mobility within same subnet
router
H1 remains in same IP subnet: IP address can remain same
switch: which AP is associated with H1?
  self-learning (Ch. 5): switch will see frame from H1 and “remember” which switch port can be used to reach H1