## Slide 1
Lab 1: Intel 80x86 Architecture
COP 3402
Fall 2014

## Slide 2
Intel 80x86 CPU Instruction Set
Memory
  8-bit bytes
  Each memory byte has 32-bit label called a physical address
  Addresses are byte addresses
  Memory size = 4,294,967,296 (2^32) bytes
bits within bytes numbered right (lsb) to left (msb) 0 to 7
+-+-+-+-+-+-+-+-+
7 6 5 4 3 2 1 0 <- bit number
bytes within word numbered right (LSB) to left (MSB) 0 to 1 - "little endian"
+--------+--------+
1 0 <- byte number
Notes: http://www4.wittenberg.edu/academics/mathcomp/shelburne/comp255/notes/Intel80x86Overview.html

## Slide 3
x86 Instruction Set
Registers:
  16 General purpose registers
Most concern to a programmer
  Registers are 16 to 32 bits long
  Internal storage that is faster and easier to access than RAM

## Slide 4
80x86 Register History
With the advent of the 32-bit 80386 processor, the 16-bit general-purpose registers, base registers, index registers, instruction pointer, and FLAGS register, but not the segment registers, were expanded to 32 bits. This is represented by prefixing an "E" (for Extended) to the register names in x86 assembly language. Thus, the AX register corresponds to the lowest 16 bits of the new 32-bit EAX register, SI corresponds to the lowest 16 bits of ESI, and so on. The general-purpose registers, base registers, and index registers can all be used as the base in addressing modes, and all of those registers except for the stack pointer can be used as the index in addressing modes.
Notes: http://en.wikipedia.org/wiki/X86

## Slide 5: Registers Format
General Purpose Registers |  |  | 
31-24 | 23-16 | 15-8 | 7-0
EAX, EBX, ECX, EDX |  |  | 
 |  | AX, BX, CX, DX | 
 |  | *H | *L
Data Registers/General Purpose
  A, B, C, D (EAX, EBX, ECX, EDX)
  EAX called accumulator (arithmetic results often go here)

## Slide 6: x86 General Register Sizes
Notes: Image courtesy of http://www.cs.virginia.edu/~evans/cs216/guides/x86.html
*

## Slide 7
Mnemonic | Length | Special Use
EAX | 32 | Accumulator; General purpose
EBX, ECX, EDX | 32 | General purpose
ESI | 32 | Source index; source address
EDI | 32 | Destination index; address of destination
ESP | 32 | Stack pointer; address of top of stack
EBP | 32 | Base pointer; address of reference point in stack
CS, DS, ES, SS, FS, GS | 16 | Selector for “Code Segment”, “Data Segment”, “Extra Segment”, “Stack Segment”, and “Additional Segments”
EIP | 32 | Instruction pointer; next instruction
EFLAGS | 32 | Collection of flags and status bits (carry, parity, zero, sign, overflow, etc.)
General Register List

## Slide 8
x86 Integers and Strings
Data Formats:
  Integers stored as binary numbers, 8 bits (byte), 16 bits (word), 32 bits (double-word), 64 bits (quadword)
    69710 = 0000 0010 1011 10012 (word)
    = 00 00 02 B916 (dword)
  2’s complement representation is used for negative values
    -56510 = 1111 1101 1100 10112 (word)
    = FF FF FD CB16 (dword)
  Characters often stored using 8-bit ASCII codes

## Slide 9: Floating Points in x86
FPU (floating point unit)
  Separate part of chip that does floating point math
  Has its own registers, separate from integer operations
  Architecture of FPU is outside scope of this class
Floating Point Format
  Sign bit: 1 bit
  Exponent width: 8-11 bits
  Significand precision/fraction: 24-53 (23-52 explicitly stored)
  Two standards: IEEE single, IEEE double
Notes: Images in the public domain, courtesy of wikipedia
*

## Slide 10: Floating Point Singles and Doubles
Single Value = (−1)sign × (1.fraction part) × 2e-127
  Max value ≈ 3.40×1038, Min value ≈ 1.18×10-38
Double Value = (−1)sign × (1.fraction part) × 2e-1023
  Max value ≈ 1.79×10308, Min value ≈ 2.23×10-308

## Slide 11: x86 Assembly Language
Instructions:
  Assembly language instructions directly converted to object code (byte code)
  Typically take the form of
    Mnemonic Operand1(trgt), Operand2(src), [Op3], [Op4]
  Typically 1 byte (but can be 2) for mnemonic opcode
  Example:
    add eax, 158 (Adds 158 to whatever is in the EAX register)

## Slide 12: x86 Instruction Set & Addressing
Instruction Set:
  Large set of instructions, commonly used mnemonics (mov, add, sub, mul, div, jmp)
  Addressing Modes
    Immediate – data in the instruction itself
    Register – data in a register
    Memory – data at some memory address
  Memory Modes
    Direct – memory location built into the instruction
    Register indirect – memory location’s address in a register

## Slide 13: Sample Program
mov eax, 36 | ; move 36 into eax register
imul eax, 9 | ; “immediate” multiple previous line by 9. eax = eax×9
mov ebx, 5 | ; divisor
cdq | ; convert ebx double to quadword (prepare for division)
idiv ebx | ; divide (implicit accumulator) by ebx. eax = eax÷5
add eax, 32 | ; eax = eax+32
mov [02CDh], eax | ; save results to memory address 02CD16
Converts temperature (36°) from Celsius to Fahrenheit
(36×9)÷5+32 = 96

## Slide 14
x86 Instruction Formatting
Instruction Formats:
Notes: *
1-5 byte addresses
*

## Slide 15
The Mod r/m byte determines the addressing mode, whether the instruction is memory to register, register to register, or register to memory and which registers are used.
MOD / R/M

## Slide 16: MOD / REG Tables
Mod | Displacement |  | 
00 | If r/m is 110, Displacement (32 bits) is address; otherwise, no displacement |  | 
01 | Eight-bit displacement, sign-extended to 32 bits |  | 
10 | 32-bit displacement (example: MOV [BX + SI]+ displacement, AL) |  | 
11 | r/m is treated as a second "reg" field |  | 
Reg | W=0 | W=1 | Double word
000 | AL | AX | EAX
001 | CL | CX | ECX
010 | DL | DX | EDX
011 | BL | BX | EBX
100 | AH | SP | ESP
101 | CH | BP | EBP
110 | DH | SI | ESI
111 | BH | DI | EDI
Notes: http://en.wikibooks.org/wiki/X86_Assembly/Machine_Language_Conversion#8086_instruction_format_.2816_bit.29
*

## Slide 17: R/M Tables
R/M | Operand Address
000 | (BX) + (SI) + displacement (0, 1, 2, or 4 bytes long)
001 | (BX) + (DI) + displacement (0, 1, 2, or 4bytes long)
010 | (BP) + (SI) + displacement (0, 1, 2, or 4bytes long)
011 | (BP) + (DI) + displacement (0, 1, 2, or 4bytes long)
100 | (SI) + displacement (0, 1, 2, or 4bytes long)
101 | (DI) + displacement (0, 1, 2, or 4bytes long)
110 | (BP) + displacement unless mod = 00 (see mod table)
111 | (BX) + displacement (0, 1, 2, or 4 bytes long)
R/M stands for Register/Memory operand.
Tells how the rest of the instruction is structured (3 bits)
Note special meaning of MOD 00, r/m 110. Normally, this would be expected to be the operand [BP]. However, instead the 32-bit displacement is treated as the absolute address. To encode the value [BP], you would use mod = 01, r/m = 110, 8-bit displacement = 0.
Notes: http://en.wikibooks.org/wiki/X86_Assembly/Machine_Language_Conversion#8086_instruction_format_.2816_bit.29
r/m Operand address
000 (BX) + (SI) + displacement (0, 1 or 2 bytes long)
001 (BX) + (DI) + displacement (0, 1 or 2 bytes long)
010 (BP) + (SI) + displacement (0, 1 or 2 bytes long)
011 (BP) + (DI) + displacement (0, 1 or 2 bytes long)
100 (SI) + displacement (0, 1 or 2 bytes long)
101 (DI) + displacement (0, 1 or 2 bytes long)
110 (BP) + displacement unless mod = 00 (see mod table)
111 (BX) + displacement (0, 1 or 2 bytes long)
*

## Slide 18: x86 Instruction Format
Example:
  xor CL, [12H]
    Exclusive Or the contents of register CL (last byte of ECX register) with contents of address 12H
    Opcode for xor is 001100dw
      d = direction = 1 because CL is the destination
      w = dword vs. byte = 0 because we are using bytes
    Code for CL is 001
    MOD = 00 (Because we have simple displacement)
    R/M = 110
  So… xor CL, [12H] =
    00110010 00001110 00010010 00000000 00000000 000000002
    32 0E 12 00 00 0016
Notes: *
http://en.wikibooks.org/wiki/X86_Assembly/Machine_Language_Conversion#8086_instruction_format_.2816_bit.29

## Slide 19: x86 Instruction Format
Example:
  add AL, 12H
    Add 12H to AL.
    Opcode for add is 00000100
    Code for AL is 000
    MOD = 11 (Because are using an immediate operation)
    reg = 110
  So… add AL, 12H =
    00000100 11110000 000100102
    04 F0 1216
opcode
mod r/m
mod
reg
r/m
00000100
11
110
000
immediate
00010010
Notes: *
http://en.wikibooks.org/wiki/X86_Assembly/Machine_Language_Conversion#8086_instruction_format_.2816_bit.29

## Slide 20: x86 Instruction Format
Example:
  add AL, BL
    Add the content of BL to AL.
    Opcode for add is 00000010
    Code for AL is 000
    Code for BL is 011
    MOD = 11 (Because we need to use r/m as a register field)
  So… add AL, BL =
    00000010 110000112
    02 C316
opcode
mod r/m
mod
reg
r/m
00000010
11
000
011
Notes: *
http://en.wikibooks.org/wiki/X86_Assembly/Machine_Language_Conversion#8086_instruction_format_.2816_bit.29