## Slide 1
COP 3402 Systems Software
Euripides Montagne
University of Central Florida
Notes: 1

## Slide 2
Eurípides Montagne
University of Central Florida
2
COP 3402 Systems Software
The processor as an instruction interpreter.

## Slide 3
Eurípides Montagne
University of Central Florida
3
Outline
The structure of a tiny computer.
A program as an isolated system.
The instruction format.
Assembly language.
Notes: 3

## Slide 4
Eurípides Montagne
University of Central Florida
4
Von-Neumann Machine (VN)
PC
MAR
A
MDR
OP ADDRESS
MEMORY
A L U
Decoder
IR

## Slide 5
Eurípides Montagne
University of Central Florida
5
Instruction Cycle
The Instruction Cycle, or Machine Cycle, in the Von-Neumann Machine (VN) is composed of 2 steps:
  1. Fetch Cycle: Instruction is retrieved from memory.
  2. Execution Cycle: Instruction is executed.
A simple Hardware Description Language will be used in order to understand how instructions are executed in VN.

## Slide 6
Eurípides Montagne
University of Central Florida
6
Definitions
Program Counter (PC) is a register that holds the address of the next instruction to be executed.
Memory Address Register (MAR) is a register used to store the address to a specific memory location in Main Storage so that data can be written to or read from that location.
Main Storage (MEM) is used to store programs and data. Random Access Memory (RAM) is a implementation of MEM.

## Slide 7
Eurípides Montagne
University of Central Florida
7
Definitions
Memory Data Register (MDR) is a register used to store data that is being sent to or received from the MEM. The data that it stores can either be in the form of instructions or simple data such as an integer.
Instruction Register (IR) is a register that stores the instruction to be executed by the processor.

## Slide 8
Eurípides Montagne
University of Central Florida
8
Definition
Arithmetic Logic Unit (ALU) is used to execute mathematical instructions such as ADD or SUB.
DECODER is a circuit that decides which instruction the processor will execute. For example, It takes the instruction op-code from the IR as input and outputs a signal to the ALU to control the execution of the ADD instruction.
Accumulator (A) is used to store data to be used as input to the ALU.

## Slide 9
Eurípides Montagne
University of Central Florida
9
Fetch-Execute Cycle
In the VN, the Instruction Cycle is defined by the following loop:
Fetch
Execute
In order to fully explain the Fetch Cycle we need to study the details of the VN data flow. The data flow consists of 4 steps.

## Slide 10
Eurípides Montagne
University of Central Florida
10
Data Movement 1
Given registers PC and MAR, the transfer of the contents of PC into MAR is indicated as:
MARPC
A
PC
MAR
MDR
OP ADDRESS
MEMORY
A L U
Decoder

## Slide 11
Eurípides Montagne
University of Central Florida
11
Data Movement 2
To transfer information from a memory location to the register MDR, we use:
MDRMEM[MAR]
The address of the memory location has been stored previously into the MAR register
PC
MAR
MDR
OP ADDRESS
MEMORY(MEM)
A L U
Decoder
A
MEM[MAR]

## Slide 12
Eurípides Montagne
University of Central Florida
12
Data Movement 2 (Cont.)
To transfer information from the MDR register to a memory location, we use:
MEM [MAR] MDR
*see previous slide for diagram
The address of the memory location has been previously stored into the MAR

## Slide 13
Eurípides Montagne
University of Central Florida
13
Data Movement 3
Transferring the contents of MDR into IR is indicated as:
IRMDR
A
PC
MAR
MDR
OP ADDRESS
MEMORY
A L U
Decoder

## Slide 14
Eurípides Montagne
University of Central Florida
14
Instruction Register Properties
The Instruction Register (IR) has two fields:
Operation (OP) and the ADDRESS.
These fields can be accessed using the selector operator “.”

## Slide 15
Eurípides Montagne
University of Central Florida
15
Data Movement 4
The Operation portion of the field is accessed as IR.OP
The operation field of the IR register is sent out to the DECODER using:
DECODERIR.OP
DECODER: If the value of IR.OP==00, then the decoder can be set to execute the fetch cycle again.

## Slide 16
Eurípides Montagne
University of Central Florida
16
Data Movement 4 Cont.
DECODERIR.OP
PC
MAR
MDR
OP ADDRESS
MEMORY
A L U
Decoder
A

## Slide 17
Eurípides Montagne
University of Central Florida
17
Instruction Cycle
The Instruction Cycle has 2 components.
Fetch Cycle which retrieves the instruction from memory.
Execution Cycle which carries out the execution of the instruction retrieved.

## Slide 18
Eurípides Montagne
University of Central Florida
18
00 Fetch Cycle
1.MAR PC
2.MDR MEM[MAR]
3.IR MDR
4.PC PC+1
5.DECODER IR.OP
Copy contents of PC into MAR
Load content of memory location into MDR
Copy value stored in MDR to IR
Increment PC Register

## Slide 19
Eurípides Montagne
University of Central Florida
19
Execution: 01 LOAD
MAR IR.ADDR
MDR MEM[MAR]
A MDR
DECODER 00
Copy the IR address value field into MAR
Load the content of a memory location into MDR
Copy content of MDR into A register
Set Decoder to execute Fetch Cycle

## Slide 20
Eurípides Montagne
University of Central Florida
20
Execution: 02 ADD
MAR IR.ADDR
MDR MEM[MAR]
A A + MDR
DECODER 00
Copy the IR address value field into MAR
Load content of memory location to MDR
Add contents of MDR and A register and store result into A
Set Decoder to execute Fetch cycle

## Slide 21
Eurípides Montagne
University of Central Florida
21
Execution: 03 STORE
MAR IR.ADDR
MDR A
MEM[MAR] MDR
DECODER 00
Copy the IR address value field into MAR
Copy A register contents into MDR
Copy content of MDR into a memory location
Set Decoder to execute fetch cycle

## Slide 22
Eurípides Montagne
University of Central Florida
22
Execution: 07 HALT
1. STOP
1. Program ends normally

## Slide 23
Eurípides Montagne
University of Central Florida
23
00 Fetch (hidden instruction)
MAR PC
MDR MEM[MAR]
IR MDR
PC PC+1
DECODER IR.OP
02 Add
MARIR.Address
MDR MEM[MAR]
A  A + MDR
DECODER 00
01 Load
MARIR.Address
MDR MEM[MAR]
A  MDR
DECODER00
03 Store
MARIR.Address
MDR A
MEM[MAR] MDR
DECODER 00
07 Halt
Instruction Set Architecture (ISA)

## Slide 24
Eurípides Montagne
University of Central Florida
24
One Address Architecture (instruction format)
The instruction format of this one-address architecture is:
OP
ADDRESS
LOAD
0000 0000 0010

## Slide 25
Eurípides Montagne
University of Central Florida
25
Instruction Set Architecture
01 - LOAD <X>
Loads the contents of memory location “X” into the A (A stands for Accumulator).
02 - ADD <X>
The data value stored at address “X” is added to the A and the result is stored back in the A.
03 - STORE <X>
Store the contents of the A into memory location “X”.
04 - SUB <X>
Subtracts the value located at address “X” from the A and stored the result back in the A.

## Slide 26
Eurípides Montagne
University of Central Florida
26
Instruction Set Architecture
05 - IN <Device #>
A value from the input device is transferred into the AC.
06 - OUT <Device #>
Print out the contents of the AC in the output device.
Device # Device
5 Keyboard
7 Printer
9 Screen
For instance you can write: 003 IN <5> “23” where “23” is the value you are typing in.

## Slide 27
Eurípides Montagne
University of Central Florida
27
Instruction Set Architecture
07 - Halt
The machine stops execution of the program.
(Return to the O.S)
08 - JMP <X>
Causes an unconditional branch to address “X”.
PC  X
09 - SKIPZ
If the contents of Accumulator = 0 then PC=PC+1 ( the next instruction is skipped).
(If the output of the ALU equals zero, the Z flag is set to 1. In this machine we test the flag and if Z = 1 the next instruction is skiped (pc= pc + 1)

## Slide 28
Eurípides Montagne
University of Central Florida
28
MAR
A
MDR
OP ADDRESS
MEMORY
A L U
Decoder
PC
If the output of the ALU equals zero, the Z flag is set to 1
0
A = 0
Z
Z =Condition Code

## Slide 29
Eurípides Montagne
University of Central Florida
29
Instruction Set Architecture
For this tiny assembly language, we are
using only one condition code (CC) Z = 0 .
Condition codes indicate the result of the most
recent arithmetic operation
Two more flags (CC) can be incorporated to test negative and positives values:
G = 1 Positive value
Z = 1 Zero
L = 1 Negative value

## Slide 30
Eurípides Montagne
University of Central Florida
30
Program State Word (condition codes - CC)
PC
Interrupt Flags
MASK
Mode
OV
MP
PI
To be defined later
I/O
TI
SVC
In addition to the Z flag, we can incorporate two more flags:
1) G meaning “greater than zero”
2) L meaning “less than zero”
CC
Z
G
L
The PSW is a register in the CPU that provides the OS with
information on the status of the running program

## Slide 31
Eurípides Montagne
University of Central Florida
31
ISA Instruction descriptions
opcode mnemonic meaning
0001 LOAD <x> A  Mem[x]
0010 ADD <x> A  A + Mem[x]
0011 STORE <x> Mem[x]  A
0100 SUB <x> A  A – Mem[x]
0101 IN <Device_#> A  read from Device
0110 OUT <Device_#> A  output to Device
0111 HALT Stop
1000 JMP <x> PC  x
1001 SKIPZ If Z = 1 Skip next instruction
1010 SKIPG If G = 1 Skip next instruction
1011 SKIPL If L = 1 Skip next instruction

## Slide 32
Eurípides Montagne
University of Central Florida
32
Assembly language Programming examples
Assign a memory location to each variable:
C  X + Y;
<000> <001> <002>
If it is necessary to use temporary memory locations, assign labels (names) to them.

## Slide 33
Eurípides Montagne
University of Central Florida
33
Assembly language Programming examples
Memory
000 1245
001 1755
002 0000
003 Load <000>
004 Add <001>
005 Store <002>
006 Halt
Memory
000 1245
001 1755
002 3000
003 Load <000>
004 Add <001>
005 Store <002>
006 Halt
After execution

## Slide 34
Eurípides Montagne
University of Central Florida
34
One Address Architecture
The instruction format of this one-address architecture consists of 16 bits: 4 bits to represent instructions and 12 bits for addresses :
OP
ADDRESS
0001
0000 0001 0001

## Slide 35
Eurípides Montagne
University of Central Florida
35
Assembler: translate symbolic code to executable code (binary)
Assembly Language
003 Load <000>
004 Add <001>
005 Store <002>
006 Halt
003 0001 0000 0000 0000
004 0010 0000 0000 0001
005 0011 0000000000010
006 0111 0000000000000
In binary
01  LOAD 06  OUT
02  ADD 07  HALT
03  STORE 08  JMP
04  SUB 09  SKIPZ
05  IN
Assembler

## Slide 36
Eurípides Montagne
University of Central Florida
36
Assembler Directives
The next step to improve our assembly language is the incorporation of pseudo-ops (assembler directives) to invoke a special service from the assembler (pseudo-operations do not generate code)
.begin  tell the assembler where the program starts
.data  to reserve a memory location.
.end  tells the assembler where the program ends.
Labels are symbolic names used to identify memory locations.

## Slide 37
Eurípides Montagne
University of Central Florida
37
Assembler Directives
This is an example of the usage of assembler directives
.begin
“Assembly language instructions”
halt (return to OS)
.data (to reserve a memory location)
.end ( tells the assembler where the program ends)
note:
the directive .end can be used to indicate where the program
starts (for example: “.end <insert label here>”

## Slide 38
Eurípides Montagne
University of Central Florida
38
Assembly language Programming examples
Label opcode address
start .begin
in x005
store a
in x005
store b
load a
sub TWO
add b
out x009
halt
a .data 0
b .data 0
TWO .data 2
.end start
Data section
Text section (code)

## Slide 39
LOAD/STORE ARCHITECTURE
A load/store architecture has a “register file” in the CPU
and it uses three instruction formats. Therefore, its assembly
language is different to the one of the accumulator machine.
OP
OP
OP
ADDRESS
ADDRESS
Ri
R i
R j
R k
JMP <address>
Load R3, <address>
Add R3, R2, R1
Notes: 39

## Slide 40
Eurípides Montagne
University of Central Florida
40
Load/Store Architecture
PC
MAR
MDR
OP
MEMORY
A L U
Decoder
R0
R1
R2
R3
+
INPUT/OUT

## Slide 41
Eurípides Montagne
University of Central Florida
41
Multiplying two numbers
Label opcode address
start .begin
in x005
store a
in x005
store b
here load result
add a
store result
load b
sub ONE
store b
skipz
jmp here
load result
out x009
halt
a .data 0
b .data 0
ONE .data 1
result .data 0
.end start
One address Architecture
(six memory access inside the loop)
Label opcode address
start .begin
in x005
store R0, a
in x005
store R0, b
load R2, result
load R3, a
load R0, b
load R1, ONE
here add R2, R2, R3
sub R0, R0, R1
skipz
jmp here
load result
out x009
halt
a .data 0
b .data 0
ONE .data 1
result .data 0
.end start
Load/Store architecture
(no memory access inside the loop)

## Slide 42
Lecture 2
Next time will talk about virtual machines
Notes: 42