## Slide 1: Hey, You, get Off of My Cloud: Exploring Information Leakage in Third-Party Compute Clouds
A paper by Thomas Ristenpart, Eran Tromer, Hovav Shacham, and Stefan Savage,
Proceedings of the ACM Conference on Computer and Communications Security, Chicago, IL, November 2009.
Presented by John Cain

## Slide 2: Cloud Computing
De-centralize software and data to scale to hardware availability
One OS
One Server
12 Operating Systems
6 servers

## Slide 3: Threat Model – Co-locating
XEN Hypervisor
Dom 0
VM1
VM2
VM3
CLOUD SERVER ##
CPU
RAM
Network
HDD

## Slide 4: Amazon EC2
Amazon EC2 cloud to find a target server
  Amazon’s EC2 operates with 2 physical regions (US and Europe)
  3 availability zones for each region
  Before beginning a VM instance you are asked to choose: the region, the availability zone and the instance-type related to hardware requirements.
  Hardware choices amount to 5 types
    32bit
      M1.small (1 ECU 1.0-1.2GHz 2007 Opteron – 1.7GB memory and 160GB storage) $.10/hr
      C1.medium
    64bit
      M1.large (2 virtual cores each with 2 ECU– 7.5GB memory and 850GB storage) $.40/hr
      M1.xlarge
      C1.xlarge

## Slide 5: Mapping the Cloud
NMAP to perform TCP Connect probes
TCP SYN traceroutes – sends TCP SYN packets with increasing TTL until no ACK is received
Map the EC2 cloud via DNS entries
  One set - External public IP DNS vs internal queries
  Second set – varied EC2 instances and checking IP
  4 distinct IP prefixes {/16, /17, /18,/19}
  14054 unique internal IPs

## Slide 6: Mapping the Cloud
  Account A
    20 instances for each availability/instance type
    92 had unique /24 prefixes
  Account B
    100 instances (20 per type) in Zone 3 (39 hours after A)
    88 unique /24 prefixes

## Slide 7: Achieving Co-Residency
Processing the data – the defining heuristic
  All IPs from /16 are from the same availability zone
  A /24 inherits any included sampled instance type
  A /24 containing a Dom0 IP address only contains Dom0 IP Addresses
  All /24s between two consecutive Dom0 inherit the former’s instance type
Dom0 IPs are consistently assigned a prefix that immediately precedes the instance IPs they are associated with –
  869 /24s in data
    Unique zone and type to 723
    23 unique zone with 2 types
    123 unlabeled

## Slide 8: Assessing Co-Residency
Network based co-residence checks
  Exploiting hard disk based covert channel between
  EC2 instances
  Co-resident if
    Matching Dom0 IP address
    Small packet round-trip times
    Numerically close internal IP addresses (within 7)
Exploiting placement
  A single account was never seen to have two instances running on a physical machine
  No more than (8) m1.small instances were running on a machine
 | Count | Median RTT (ms)
Co-resident Instance | 62 | 0.242
Zone1 Crl A Zone1 Crl B | 62 62 | 1.164 1.027
Zone2 Crl A Zone2 Crl B | 61 62 | 1.113 1.187
Zone3 Crl A Zone3 Crl B | 62 62 | .550 .436

## Slide 9: Instance Placement - Abuse
Brute Force
  Run numerous instances over a long period of time - determine amount of instances that were able to form co-residence with
  Using the ‘cloud map’ Zone 3 / m1.small (1686 servers)
    78 unique Dom0 IPs
    1785 instance probes
    141 victim servers were hit (8.4% coverage)
Instance Flooding
  Abuse scalable infrastructures – when service scales to meet demand determine server and try to join it
  Instances tend to restart on the same physical server
  New instances started after an instance starts will tend to be placed nearby
  A single account will not have more than 1 instance started on a single platform

## Slide 10: Side Channel Abuse
Cross VM leakage
  Stealing crypto keys through cache-based side channels
  Denial of service by attacker instance physical resource usage
Cache-based covert channel
  Sender idles to transmit “0” and accesses memory to transmit “1”
  Receiver accesses memory block and observes the latencies perceived to be flushing of the cache
Estimating Traffic Rates
Keystroke Timing Attack
  Similar to cache-based load measurements
  Hope to catch password input via shell and detect the time in between keys to gather length

## Slide 11: Contribution
This paper contributes greatly to the understanding of mapping of the EC2 cloud both in practical application and in cloud security
The authors include commentary in each section expressing the validity of each attack attempt and the ease to correct it
Shows the robust nature of the EC2 cloud –
  Easiest option for commercial ventures is to pick a M1.xlarge or CL1.xlarge as they fill the entire physical platform and deny co-residence
  Xen’s resource exclusion is not perfect but nearly impossible to exploit – improved with software randomization tweaks to cache

## Slide 12: Weakness
Mapping was mostly at random, co-residence was extremely low even with techniques applied
Instance placement was time sensitive which is constantly updating and changing
With the exception of one m1.large instance, only m1.smalls are able to co-reside and not really applicable to commercial applications
The side channel analysis was weak and speculative; they didn’t seem to run any hard penetration testing utilities but focused on very low level cpu-cache analysis

## Slide 13: Improvement
This idea could be improved with more financial resources to run hundreds of accounts with the maximum 20 instances all at the same time
Taking further the idea of side-channel attacks to combine traditional attacks with having co-located instances. This could make the extremely small bandwidth side channels they were able to exploit more practicable. With resource starvation traditional attacks might be more effective
Poisoning dom0 resource mapping to gain further access

## Slide 14: Conclusion
My thoughts –
  project was mostly unsuccessful in demonstrating anything actionable
  The EC2 cloud is potentially dangerous for how accessible it makes gaining access to vast computational and bandwidth resources for launching attacks on other networks
  Thanks