## Slide 1: Data and Computer Communications
Tenth Edition
by William Stallings
Notes: “Data and Computer Communications”, 10/e, by William Stallings, Chapter 10 “Cellular Wireless Network”.

## Slide 2: Cellular Wireless Network Modified by Cliff Zou (UCF)
Chapter 10
Notes: Of all the tremendous advances in data communications and telecommunications,
perhaps the most revolutionary is the development of cellular networks .
Cellular technology is the foundation of mobile wireless communications
and supports users in locations that are not easily served by wired networks.
Cellular technology is the underlying technology for mobile telephones,
personal communications systems, wireless Internet and wireless Web applications,
and much more.
We begin this chapter with a look at the basic principles used in all cellular
networks. Then we look at specific cellular technologies and standards, which
are conveniently grouped into four generations. Finally, we examine LTE-Advanced,
which is the standard for the fourth generation, in more detail.

## Slide 3: Principles of Cellular Networks
Developed to increase the capacity available for mobile radio telephone service
Prior to cellular radio:
  Mobile service was only provided by a high powered transmitter/receiver
  Typically supported about 25 channels
  Had an effective radius of about 80km
Notes: Cellular radio is a technique that was developed to increase the capacity available for mobile radio telephone service. Prior to the introduction of cellular radio, mobile radio telephone service was only provided by a high-power transmitter/receiver. A typical system would support about 25 channels with an effective radius of about 80 km. The way to increase the capacity of the system is to use lower-power systems with shorter radius and to use numerous transmitters/receivers.

## Slide 4: Cellular Network Organization
Key for mobile technologies
Based on the use of multiple low power transmitters (<100 W)
Area divided into cells
  In a tiling pattern to provide full coverage
  Each one with its own antenna
  Each is allocated its own range of frequencies
  Served by a base station
    Consisting of transmitter, receiver, and control unit
  Adjacent cells are assigned different frequencies to avoid interference or crosstalk
    Cells sufficiently distant from each other can use the same frequency band
Notes: The essence of a cellular network is the use of multiple low-power transmitters, on the order of 100 W or less. Because the range of such a transmitter is small, an area can be divided into cells, each one served by its own antenna. Each cell is allocated a band of frequencies and is served by a base station, consisting of transmitter, receiver, and control unit. Adjacent cells are assigned different frequencies to avoid interference or crosstalk. However, cells sufficiently distant from each other can use the same frequency band.

## Slide 5
Notes: The first design decision to make is the shape of cells to cover an area. A matrix of square cells would be the simplest layout to define (Figure 10.1a). However, this geometry is not ideal. If the width of a square cell is d, then a cell has four neighbors at a distance d and four neighbors at a distance √2d. As a mobile user within a cell moves toward the cell's boundaries, it is best if all of the adjacent antennas are equidistant. This simplifies the task of determining when to switch the user to an adjacent antenna and which antenna to choose. A hexagonal pattern provides for equidistant antennas (Figure 10.1b). The radius of a hexagon is defined to be the radius of the circle that circumscribes it (equivalently, the distance from the center to each vertex; also equal to the length of a side of a hexagon). For a cell radius R, the distance between the cell center and each adjacent cell center is d = √3R.
In practice, a precise hexagonal pattern is not used. Variations from the ideal are due to topographical limitations, local signal propagation conditions, and practical limitation on sitting antennas.
A wireless cellular system limits the opportunity to use the same frequency for different communications because the signals, not being constrained, can interfere with one another even if geographically separated. Systems supporting a large number of communications simultaneously need mechanisms to conserve spectrum.

## Slide 6: Frequency Reuse
Object is to share nearby (but not adjacent) cell frequencies without interfering with each other
Allows multiple simultaneous conversations
10 to 50 frequencies per cell
Power of base transceiver controlled
Allow communications within cell on given frequency
Limit escaping power to adjacent cells
Notes: In a cellular system, each cell has a base transceiver. The transmission power is carefully controlled (to the extent that it is possible in the highly variable mobile communication environment) to allow communication within the cell using a given frequency while limiting the power at that frequency that escapes the cell into adjacent ones. The objective is to use the same frequency in other nearby (but not adjacent) cells, thus allowing the frequency to be used for multiple simultaneous conversations. Generally, 10 to 50 frequencies are assigned to each cell, depending on the traffic expected.

## Slide 7
Notes: The essential issue is to determine how many cells must intervene between two cells using the same frequency so that the two cells do not interfere with each other. Various patterns of frequency reuse are possible. Figure 10.2 shows some examples. If the pattern consists of N cells and each cell is assigned the same number of frequencies, each cell can have K/N frequencies, where K is the total number of frequencies allotted to the system.
In characterizing frequency reuse, the following parameters are commonly used:
D = minimum distance between centers of cells that use the same band of frequencies (called cochannels)
R = radius of a cell
d = distance between centers of adjacent cells (d = √3R)
N = number of cells in a repetitious pattern (each cell in the pattern uses a unique band of frequencies), termed the reuse factor

## Slide 8: Increasing Capacity
Add new channels
  Not all channels used to start with
Frequency borrowing
  Taken from adjacent cells by congested cells
  Assign frequencies dynamically
Cell splitting
  Non-uniform topography and traffic distribution
  Use smaller cells in high use areas
Notes: In time, as more customers use the system, traffic may build up so that there are not enough frequencies assigned to a cell to handle its calls. A number of approaches have been used to cope with this situation, including the following:
Adding new channels: Typically, when a system is set up in a region, not all of the channels are used, and growth and expansion can be managed in an orderly fashion by adding new channels.
Frequency borrowing: In the simplest case, frequencies are taken from adjacent cells by congested cells. The frequencies can also be assigned to cells dynamically.
Cell splitting: In practice, the distribution of traffic and topographic features is not uniform, and this presents opportunities for capacity increase. Cells in areas of high usage can be split into smaller cells. Generally, the original cells are about 6.5 to 13 km in size. The smaller cells can themselves be split; however, 1.5-km cells are close to the practical minimum size as a general solution (but see the subsequent discussion of microcells).

## Slide 9
Notes: To use a smaller cell, the power level used must be reduced to keep the signal within the cell. Also, as the mobile units move, they pass from cell to cell, which requires transferring of the call from one base transceiver to another. This process is called a handoff. As the cells get smaller, these handoffs become much more frequent. Figure 10.3 indicates schematically how cells can be divided to provide more capacity. A radius reduction by a factor of F reduces the coverage area and increases the required number of base stations by a factor of F2.

## Slide 10: Increasing Capacity
Cell sectoring
Cell is divided into wedge shaped sectors (3–6 per cell)
Microcells
As cells become smaller, antennas move from tops of hills and large buildings to tops of small buildings and sides of large buildings, to lamp posts, where they form microcells
Each sector is assigned a separate subset of the cell’s channels
Directional antennas at base station are used to focus on each sector
Use reduced power to cover a much smaller area
Good for city streets in congested areas, along highways, inside large public buildings
Notes: Cell sectoring: With cell sectoring, a cell is divided into a number of wedge-shaped sectors, each with its own set of channels, typically three or six sectors per cell. Each sector is assigned a separate subset of the cell's channels, and directional antennas at the base station are used to focus on each sector.
Microcells: As cells become smaller, antennas move from the tops of tall buildings or hills, to the tops of small buildings or the sides of large buildings, and finally to lamp posts, where they form microcells. Each decrease in cell size is accompanied by a reduction in the radiated power levels from the base stations and the mobile units. Microcells are useful in city streets in congested areas, along highways, and inside large public buildings.

## Slide 11
Notes: Assume a system of 32 cells with a cell radius of 1.6 km, a total of 32 cells, a total frequency bandwidth that supports 336 traffic channels, and a reuse factor of N = 7. If there are 32 total cells, what geographic area is covered, how many channels are there per cell, and what is the total number of concurrent calls that can be handled? Repeat for a cell radius of 0.8 km and 128 cells.
Figure 10.4a shows an approximately square pattern.

## Slide 12
Notes: Figure 10.5 shows the principal elements of a cellular system. In the approximate center of each cell is a base station (BS). The BS includes one or more antennas, a controller, and a number of transceivers, for communicating on the channels assigned to that cell. The controller is used to handle the call process between the mobile unit and the rest of the network. At any time, a number of mobile user units may be active and moving about within a cell, communicating with the BS. Each BS is connected to a mobile telecommunications switching office (MTSO), with one MTSO serving multiple BSs. Typically, the link between an MTSO and a BS is by a wire line, although a wireless link is also possible. The MTSO connects calls between mobile units. The MTSO is also connected to the public telephone or telecommunications network and can make a connection between a fixed subscriber to the public network and a mobile subscriber to the cellular network. The MTSO assigns the voice channel to each call, performs handoffs, and monitors the call for billing information.

## Slide 13: Cellular System Channels
Two types of channels are available between mobile unit and base station (BS)
Control Channels
Establish relationship between mobile unit and nearest base station
Traffic Channels
Carry voice and data
Set up and maintain calls
Notes: The use of a cellular system is fully automated and requires no action on the part of the user other than placing or answering a call. Two types of channels are available between the mobile unit and the base station (BS): control channels and traffic channels. Control channels are used to exchange information having to do with setting up and maintaining calls and with establishing a relationship between a mobile unit and the nearest BS. Traffic channels carry a voice or data connection between users.

## Slide 14
Notes: Figure 10.6 illustrates the steps in a typical call between two mobile users within an area controlled by a single MTSO:
Mobile unit initialization: When the mobile unit is turned on, it scans and selects the strongest setup control channel used for this system (Figure 10.6a). Cells with different frequency bands repetitively broadcast on different setup channels. The receiver selects the strongest setup channel and monitors that channel. The effect of this procedure is that the mobile unit has automatically selected the BS antenna of the cell within which it will operate. Then a handshake takes place between the mobile unit and the MTSO controlling this cell, through the BS in this cell. The handshake is used to identify the user and register its location. As long as the mobile unit is on, this scanning procedure is repeated periodically to account for the motion of the unit. If the unit enters a new cell, then a new BS is selected. In addition, the mobile unit is monitoring for pages, discussed subsequently.
Mobile-originated call: A mobile unit originates a call by sending the number of the called unit on the preselected setup channel (Figure 10.6b). The receiver at the mobile unit first checks that the setup channel is idle by examining information in the forward (from the BS) channel. When an idle is detected, the mobile may transmit on the corresponding reverse (to BS) channel. The BS sends the request to the MTSO.
Paging: The MTSO then attempts to complete the connection to the called unit. The MTSO sends a paging message to certain BSs depending on the called mobile number (Figure 10.6c). Each BS transmits the paging signal on its own assigned setup channel.
Call accepted: The called mobile unit recognizes its number on the setup channel being monitored and responds to that BS, which sends the response to the MTSO. The MTSO sets up a circuit between the calling and called BSs. At the same time, the MTSO selects an available traffic channel within each BS's cell and notifies each BS, which in turn notifies its mobile unit (Figure 10.6d). The two mobile units tune to their respective assigned channels.
Ongoing call: While the connection is maintained, the two mobile units exchange voice or data signals, going through their respective BSs and the MTSO (Figure 10.6e).
Handoff: If a mobile unit moves out of range of one cell and into the range of another during a connection, the traffic channel has to change to one assigned to the BS in the new cell (Figure 10.6f). The system makes this change without either interrupting the call or alerting the user.

## Slide 15: Other Functions
Call blocking
  After repeated attempts, if all traffic channels are busy, a busy tone is returned
Call termination
  When a user hangs up channels at the BS are released
Call drop
  When BS cannot maintain required signal strength
Calls to/from fixed and remote mobile subscriber
  MTSO connects to the PSTN
Notes: Other functions performed by the system but not illustrated in Figure 10.6 include:
Call blocking: During the mobile-initiated call stage, if all the traffic channels assigned to the nearest BS are busy, then the mobile unit makes a preconfigured number of repeated attempts. After a certain number of failed tries, a busy tone is returned to the user.
Call termination: When one of the two users hangs up, the MTSO is informed and the traffic channels at the two BSs are released.
Call drop: During a connection, because of interference or weak signal spots in certain areas, if the BS cannot maintain the minimum required signal strength for a certain period of time, the traffic channel to the user is dropped and the MTSO is informed.
Calls to/from fixed and remote mobile subscriber: The MTSO connects to the public switched telephone network. Thus, the MTSO can set up a connection between a mobile user in its area and a fixed subscriber via the telephone network. Further, the MTSO can connect to a remote MTSO via the telephone network or via dedicated lines and set up a connection between a mobile user in its area and a remote mobile user.

## Slide 16: Mobile Radio Propagation Effects
Signal strength
  Strength of signal between BS and mobile unit needs to be strong enough to maintain signal quality
  Not too strong so as to create co-channel interference
  Must handle variations in noise
Fading
  Time variation of received signal
  Caused by changes in transmission path(s)
  Even if signal strength is in effective range, signal propagation effects may disrupt the signal
Notes: Mobile radio communication introduces complexities not found in wire communication or in fixed wireless communication. Two general areas of concern are signal strength and signal propagation effects.
Signal strength: The strength of the signal between the base station and the mobile unit must be strong enough to maintain signal quality at the receiver but no so strong as to create too much co-channel interference with channels in another cell using the same frequency band. Several complicating factors exist. Human-made noise varies considerably, resulting in a variable noise level. For example, automobile ignition noise in the cellular frequency range is greater in the city than in a suburban area. Other signal sources vary from place to place. The signal strength varies as a function of distance from the BS to a point within its cell. Moreover, the signal strength varies dynamically as the mobile unit moves.
Fading: Even if signal strength is within an effective range, signal propagation effects may disrupt the signal and cause errors. Fading is discussed subsequently in this section.

## Slide 17: Design Factors
Propagation effects:
  Desired maximum transmit power level at BS and mobile units
  Typical height of mobile unit antenna
  Available height of the BS antenna
Propagation effects are dynamic and difficult to predict
  Use model based on empirical data
    Widely used model developed by Okumura and refined by Hata
      Detailed analysis of Tokyo area
      Produced path loss information for an urban environment
  Hata's model is an empirical formulation that takes into account a variety of conditions
Notes: In designing a cellular layout, the communications engineer must take account of these various propagation effects, the desired maximum transmit power level at the base station and the mobile units, the typical height of the mobile unit antenna, and the available height of the BS antenna. These factors will determine the size of the individual cell. Unfortunately, as just described, the propagation effects are dynamic and difficult to predict. The best that can be done is to come up with a model based on empirical data and to apply that model to a given environment to develop guidelines for cell size. One of the most widely used models was developed by Okumura et al [OKUM68] and subsequently refined by Hata [HATA80]. The original was a detailed analysis of the Tokyo area and produced path loss information for an urban environment. Hata's model is an empirical formulation that takes into account a variety of environments and conditions
The Okumura/Hata model is considered to be among the best in terms of accuracy in path loss prediction and provides a practical means of estimating path loss in a wide variety of situations [FREE07].

## Slide 18
Notes: Three propagation mechanisms, illustrated in Figure 10.7, play a role. Reflection occurs when an electromagnetic signal encounters a surface that is large relative to the wavelength of the signal. For example, suppose a ground-reflected wave near the mobile unit is received. Because the ground-reflected wave has a 180º phase shift after reflection, the ground wave and the line-of-sight (LOS) wave may tend to cancel, resulting in high signal loss. Further, because the mobile antenna is lower than most human-made structures in the area, multipath interference occurs. These reflected waves may interfere constructively or destructively at the receiver.
Diffraction occurs at the edge of an impenetrable body that is large compared to the wavelength of the radio wave. When a radio wave encounters such an edge, waves propagate in different directions with the edge as the source. Thus, signals can be received even when there is no unobstructed LOS from the transmitter.
If the size of an obstacle is on the order of the wavelength of the signal or less, scattering occurs. An incoming signal is scattered into several weaker outgoing signals. At typical cellular microwave frequencies, there are numerous objects, such as lamp posts and traffic signs, that can cause scattering. Thus, scattering effects are difficult to predict.
These three propagation effects influence system performance in various ways
depending on local conditions and as the mobile unit moves within a cell. If a mobile
unit has a clear LOS to the transmitter, then diffraction and scattering are generally
minor effects, although reflection may have a significant impact. If there is no clear
LOS, such as in an urban area at street level, then diffraction and scattering are the
primary means of signal reception.

## Slide 19
Notes: As just noted, one unwanted effect of multipath propagation is that multiple copies of a signal may arrive at different phases. If these phases add destructively, the signal level relative to noise declines, making signal detection at the receiver more difficult.
A second phenomenon, of particular importance for digital transmission, is intersymbol interference (ISI). Consider that we are sending a narrow pulse at a given frequency across a link between a fixed antenna and a mobile unit. Figure 10.8 shows what the channel may deliver to the receiver if the impulse is sent at two different times. The upper line shows two pulses at the time of transmission. The lower line shows the resulting pulses at the receiver. In each case the first received pulse is the desired LOS signal. The magnitude of that pulse may change because of changes in atmospheric attenuation. Further, as the mobile unit moves farther away from the fixed antenna, the amount of LOS attenuation increases. But in addition to this primary pulse, there may be multiple secondary pulses due to reflection, diffraction, and scattering. Now suppose that this pulse encodes one or more bits of data. In that case, one or more delayed copies of a pulse may arrive at the same time as the primary pulse for a subsequent bit. These delayed pulses act as a form of noise to the subsequent primary pulse, making recovery of the bit information more difficult.
As the mobile antenna moves, the location of various obstacles changes; hence the number, magnitude, and timing of the secondary pulses change. This makes it difficult to design signal processing techniques that will filter out multipath effects so that the intended signal is recovered with fidelity.

## Slide 20: Types of Fading
Fast fading
Rapid variations in signal strength occur over distances of about one-half a wavelength
Slow fading
Change in the average received power level due to user passing different height buildings, vacant lots, intersections, etc.
Flat fading
All frequency components of the received signal fluctuate in the same proportions simultaneously
Selective fading
Attenuation occurring over a portion of the bandwidth of the signal
Notes: Fading effects in a mobile environment can be classified as either fast or slow. Referring to Figure 10.7, as the mobile unit moves down a street in an urban environment, rapid variations in signal strength occur over distances of about one-half a wavelength. At a frequency of 900 MHz, which is typical for mobile cellular applications, a wavelength is 0.33 m. Changes of amplitude can be as much as 20 or 30 dB over a short distance. This type of rapidly changing fading phenomenon, known as fast fading, affects not only mobile phones in automobiles, but even a mobile phone user walking down an urban street.
As the mobile user covers distances well in excess of a wavelength, the urban environment changes, as the user passes buildings of different heights, vacant lots, intersections, and so forth. Over these longer distances, there is a change in the average received power level about which the rapid fluctuations occur. This is referred to as slow fading.
Fading effects can also be classified as flat or selective. Flat fading, or nonselective fading, is that type of fading in which all frequency components of the received signal fluctuate in the same proportions simultaneously. Selective fading affects unequally the different spectral components of a radio signal. The term selective fading is usually significant only relative to the bandwidth of the overall communications channel. If attenuation occurs over a portion of the bandwidth of the signal, the fading is considered to be selective; nonselective fading implies that the signal bandwidth of interest is narrower than, and completely covered by, the spectrum affected by the fading.

## Slide 21: Error Compensation Mechanisms
Forward error correction
  Applicable in digital transmission applications
  The ratio of total bits sent to data bits sent is between 2-3
Adaptive equalization
  Applied to transmissions that carry analog or digital information
  Used to combat intersymbol interference
  Involves gathering the dispersed symbol energy back together into its original time interval
Notes: The efforts to compensate for the errors and distortions introduced by multipath fading fall into three general categories: forward error correction, adaptive equalization, and diversity techniques. In the typical mobile wireless environment, techniques from all three categories are combined to combat the error rates encountered.
Forward error correction is applicable in digital transmission applications: those in which the transmitted signal carries digital data or digitized voice or video data. Typically in mobile wireless applications, the ratio of total bits sent to data bits sent is between 2 and 3. This may seem an extravagant amount of overhead, in that the capacity of the system is cut to one-half or one-third of its potential, but the mobile wireless environment is so difficult that such levels of redundancy are necessary. Chapter 6 discusses forward error correction.
Adaptive equalization can be applied to transmissions that carry analog information (e.g., analog voice or video) or digital information (e.g., digital data, digitized voice or video) and is used to combat intersymbol interference. The process of equalization involves some method of gathering the dispersed symbol energy back together into its original time interval. Equalization is a broad topic; techniques include the use of so-called lumped analog circuits as well as sophisticated digital signal processing algorithms.

## Slide 22: Error Compensation Mechanisms
Diversity
Based on the fact that individual channels experience independent fading events
Use multiple logical channels between transmitter and receiver
Send part of signal over each channel
Doesn’t eliminate errors, but reduces
Space diversity involves physical transmission paths
More commonly refers to frequency or time diversity
Most important example of frequency diversity is spread spectrum
Notes: Diversity is based on the fact that individual channels experience independent fading events. We can therefore compensate for error effects by providing multiple logical channels in some sense between transmitter and receiver and sending part of the signal over each channel. This technique does not eliminate errors but it does reduce the error rate, since we have spread the transmission out to avoid being subjected to the highest error rate that might occur. The other techniques (equalization, forward error correction) can then cope with the reduced error rate.
Some diversity techniques involve the physical transmission path and are referred to as space diversity. For example, multiple nearby antennas may be used to receive the message, with the signals combined in some fashion to reconstruct the most likely transmitted signal. Another example is the use of collocated multiple directional antennas, each oriented to a different reception angle with the incoming signals again combined to reconstitute the transmitted signal.
More commonly, the term diversity refers to frequency diversity or time diversity techniques. With frequency diversity, the signal is spread out over a larger frequency bandwidth or carried on multiple frequency carriers. The most important example of this approach is spread spectrum, which is examined in Chapter 17.

## Slide 23: Table 10.1 Wireless Network Generations
Notes: Since their introduction in the mid-1980s, cellular networks have evolved rapidly.
For convenience, industry and standards bodies group the technical advances into
“generations.” We are now up to the fourth generation (4G) of cellular network
technology. In this section, we give a brief overview of the first three generations.
The following section is devoted to 4G.
Table 10.1 lists some of the key characteristics of the cellular network
generations.

## Slide 24: First Generation (1G)
Original cellular telephone networks
Analog traffic channels
Designed to be an extension of the public switched telephone networks
The most widely deployed system was the Advanced Mobile Phone Service (AMPS)
Also common in South America, Australia, and China
Notes: The original cellular telephone networks provided analog traffic channels; these are now referred to as first-generation systems. Since the early 1980s the most common first-generation system in North America has been the Advanced Mobile Phone Service (AMPS) developed by AT&T. This approach is also common in South America, Australia, and China.
In North America, two 25-MHz bands were allocated to AMPS, one for transmission
from the base station to the mobile unit (869–894 MHz) and the other for
transmission from the mobile to the base station (824–849 MHz). Each of these
bands is split in two to encourage competition (i.e., in each market two operators can
be accommodated). An operator is allocated only 12.5 MHz in each direction for its
system. The channels are spaced 30 kHz apart, which allows a total of 416 channels
per operator. Twenty-one channels are allocated for control, leaving 395 to carry
calls. The control channels are data channels operating at 10 kbps. The conversation
channels carry the conversations in analog using frequency modulation (FM). Simple
FDMA is used to provide multiple access. Control information is also sent on the
conversation channels in bursts as data. This number of channels
is inadequate for most major markets, so some way must be found either to use less bandwidth per
conversation or to reuse frequencies. Both approaches have been taken in the various
approaches to 1G telephony. For AMPS, frequency reuse is exploited.

## Slide 25: Second Generation (2G)
Developed to provide higher quality signals, higher data rates for support of digital services, and greater capacity
Key differences between 1G and 2G include:
  Digital traffic channels
  Encryption
  Error detection and correction
  Channel access
    Time division multiple access (TDMA)
    Code division multiple access (CDMA)
Notes: First-generation cellular networks, such as AMPS, quickly became highly popular, threatening to swamp available capacity. Second-generation systems have been developed to provide higher quality signals, higher data rates for support of digital services, and greater capacity. [BLAC99b] lists the following as the key differences between the two generations:
Digital traffic channels: The most notable difference between the two generations is that first-generation systems are almost purely analog, whereas second-generation systems are digital. In particular, the first-generation systems are designed to support voice channels using FM; digital traffic is supported only by the use of a modem that converts the digital data into analog form. Second-generation systems provide digital traffic channels. These readily support digital data; voice traffic is first encoded in digital form before transmitting.
Encryption: Because all of the user traffic, as well as control traffic, is digitized in second-generation systems, it is a relatively simple matter to encrypt all of the traffic to prevent eavesdropping. All second-generation systems provide this capability, whereas first-generation systems send user traffic in the clear, providing no security.
Error detection and correction: The digital traffic stream of second-generation systems also lends itself to the use of error detection and correction techniques, such as those discussed in Chapters 6 and 16. The result can be very clear voice reception.
Channel access: In first-generation systems, each cell supports a number of channels. At any given time a channel is allocated to only one user. Second-generation systems also provide multiple channels per cell, but each channel is dynamically shared by a number of users using time division multiple access (TDMA) or code division multiple access (CDMA).

## Slide 26: Third Generation (3G)
Objective is to provide high-speed wireless communications to support multimedia, data, and video in addition to voice
3G capabilities:
Voice quality comparable to PSTN
144 kbps available to users in high-speed motor vehicles over large areas
384 kbps available to pedestrians standing or moving slowly over small areas
Support for 2.048 Mbps for office use
Symmetrical and asymmetrical data rates
Support for both packet-switched and circuit-switched data services
Adaptive interface to Internet
More efficient use of available spectrum
Support for a wide variety of mobile equipment
Flexibility to allow the introduction of new services and technologies
Notes: The objective of the third generation (3G) of wireless communication is to provide fairly high-speed wireless communications to support multimedia, data, and video in addition to voice. The ITU’s International Mobile Telecommunications for the year 2000 (IMT-2000) initiative has defined the third-generation capabilities as:
Voice quality comparable to the public switched telephone network
144 kbps data rate available to users in high-speed motor vehicles over large areas
384 kbps available to pedestrians standing or moving slowly over small areas
Support (to be phased in) for 2.048 Mbps for office use
Symmetrical and asymmetrical data transmission rates
Support for both packet-switched and circuit-switched data services
An adaptive interface to the Internet to reflect efficiently the common asymmetry between inbound and outbound traffic
More efficient use of the available spectrum in general
Support for a wide variety of mobile equipment
Flexibility to allow the introduction of new services and technologies

## Slide 27: CDMA
Dominant technology for 3G systems
Chip rate
  Given bandwidth, chip rate depends on desired data rate, need for error control, and bandwidth limitations
  Chip rate of 3 Mcps or more is reasonable
CDMA schemes:
Bandwidth (limit channel to 5 MHz)
5 MHz reasonable upper limit on what can be allocated for 3G
5 MHz is adequate for supporting data rates of 144 and 384 kHz
Notes: The dominant technology for 3G systems is CDMA. Although three different CDMA schemes have been adopted, they share some common design issues
Bandwidth: An important design goal for all 3G systems is to limit channel usage to 5 MHz. There are several reasons for this goal. On the one hand, a bandwidth of 5 MHz or more improves the receiver's ability to resolve multipath when compared to narrower bandwidths. On the other hand, available spectrum is limited by competing needs, and 5 MHz is a reasonable upper limit on what can be allocated for 3G. Finally, 5 MHz is adequate for supporting data rates of 144 and 384 kHz, the main targets for 3G services.
Chip rate: Given the bandwidth, the chip rate depends on desired data rate, the need for error control, and bandwidth limitations. A chip rate of 3 Mcps or more is reasonable given these design parameters.

## Slide 28: CDMA – Multirate
Provision of multiple fixed-data-rate channels to user
Different data rates provided on different logical channels
Logical channel traffic can be switched independently through wireless and fixed networks to different destinations
Can flexibly support multiple simultaneous applications
Can efficiently use available capacity by only providing the capacity required for each service
Notes: The term multirate refers to the provision of multiple fixed-data-rate
logical channels to a given user, in which different data rates are provided on
different logical channels. Further, the traffic on each logical channel can be
switched independently through the wireless and fixed networks to different
destinations. The advantage of multirate is that the system can flexibly support
multiple simultaneous applications from a given user and can efficiently use
available capacity by only providing the capacity required for each service.

## Slide 29: Fourth Generation (4G)
Provide ultra-broadband Internet access for a variety of mobile devices including laptops, smartphones, and tablet PCs
Support Mobile Web access and high-bandwidth applications such as high-definition mobile TV, mobile video conferencing, and gaming services
Designed to maximize bandwidth and throughput while also maximizing spectral efficiency
Minimum requirements:
Be based on an all-IP packet switched network
Support peak data rates of up to approximately 100 Mbps for high-mobility mobile access and up to approximately 1 Gbps for low-mobility access such as local wireless access
Dynamically share and use the network resources to support more simultaneous users per cell
Support smooth handovers across heterogeneous networks
Support high quality of service for next-generation multimedia applications
LTE is OFDMA-based
Notes: The evolution of smartphones and cellular networks has ushered in a new generation
of capabilities and standards, which is collectively called 4G. 4G systems
provide ultra-broadband Internet access for a variety of mobile devices including
laptops, smartphones, and tablet PCs. 4G networks support Mobile Web access and
high-bandwidth applications such as high-definition mobile TV, mobile video conferencing,
and gaming services.
These requirements have led to the development of a fourth generation (4G)
of mobile wireless technology that is designed to maximize bandwidth and throughput
while also maximizing spectral efficiency. The ITU has issued directives for 4G
networks. According to the ITU, an IMT-Advanced (or 4G) cellular system must
fulfill a number of minimum requirements, including the following:
• Be based on an all-IP packet switched network.
• Support peak data rates of up to approximately 100 Mbps for high-mobility
mobile access and up to approximately 1 Gbps for low-mobility access such as
local wireless access.
• Dynamically share and use the network resources to support more simultaneous
users per cell.
• Support smooth handovers across heterogeneous networks.
• Support high quality of service for next-generation multimedia applications.
In contrast to earlier generations, 4G systems do not support traditional
circuit-switched telephony service, providing only IP telephony services. And,
as may be observed in Table 10.1, the spread spectrum radio technologies that
characterized 3G systems are replaced in 4G systems by OFDMA (orthogonal frequency-
division multiple access) multicarrier transmission and frequency-domain
equalization schemes.

## Slide 30
Notes: Figure 10.9 illustrates several major differences between 3G and 4G cellular
networks. As shown in Figure 10.9a, the connections between base stations and
switching offices in 3G networks are typically cable-based, either copper or fiber
wires. Circuit switching is supported to enable voice connections between mobile
users and phones connected to the PSTN. Internet access in 3G networks may also
be routed through switching offices. By contrast, in 4G networks, IP telephony
is the norm as are IP packet-switched connections for Internet access. These are
enabled by wireless connections, such as fixed broadband wireless access (BWA)
WiMAX, between base stations and switching offices (Figure 10.9b). Connections
among mobile users with 4G-capable smartphones may never be routed over cable-based,
circuit-switched connections—all communications between them can be
IP-based and handled by wireless links. This setup facilitates deployment of mobile-to-
mobile video call/video conferencing services and the simultaneous delivery of
voice and data services (such as Web browsing while engaged in a phone call). 4G
mobile users can still connect with 3G network users and PSTN subscribers over
cable/fiber circuit-switched connections between the switching offices.

## Slide 31: LTE - Advanced
  Based on use of orthogonal frequency division multiple access (OFDMA)
Two candidates have emerged for 4G standardization:
Long Term Evolution (LTE)
Developed by the Third Generation Partnership Project (3GPP), a consortium of North American, Asian, and European telecommunications standards organizations
WiMax
(from the IEEE 802.16 committee)
Notes: Two candidates emerged for 4G standardization. One is known as Long Term
Evolution (LTE) , which has been developed by the Third Generation Partnership
Project (3GPP), a consortium of Asian, European, and North American telecommunications
standards organizations. The other effort is from the IEEE 802.16 committee,
which has developed standards for high-speed fixed wireless operations known as
WiMAX (described in Chapter 18). The committee has specified an enhancement
of WiMAX to meet 4G needs. The two efforts are similar in terms of both performance
and technology. Both are based on the use of orthogonal frequency-division
multiple access (OFDMA) to support multiple access to network resources. WiMAX
uses a pure OFDMA approach of both uplink (UL) and downlink (DL). LTE uses
pure OFDMA on the downlink but a technique that is based on OFDMA offers
enhanced power efficiency for the uplink. While WiMAX retains a role as the technology
for fixed broadband wireless access, LTE has become the universal standard
for 4G wireless. For example, all of the major carriers in the United States, including
AT&T and Verizon, have adopted a version of LTE based on frequency-division
duplex (FDD), whereas China Mobile, the world’s largest telecommunication carrier,
has adopted a version of LTE based on time-division duplex (TDD).

## Slide 32: Table 10.2 Comparison of Performance Requirements for LTE (3G) and LTE-Advanced (4G)
Notes: LTE development began in the 3G era and its initial releases provided 3G
or enhanced 3G services. Beginning with release 10, LTE provides a 4G service,
known as LTE-Advanced . Table 10.2 compares the performance goals of LTE and
LTE-Advanced.

## Slide 33
Notes: Figure 10.10 illustrates the principal elements in an LTE-Advanced network. The
heart of the system is the base station, designated evolved NodeB (eNodeB) . In
LTE, the base station is referred to as NodeB. The key differences between the two
base station technologies are:
• The NodeB station interface with subscriber stations (referred to as user
equipment (UE)) is based on CDMA, whereas the eNodeB air interface is
based on OFDMA.
• eNodeB embeds its own control functionality, rather than using an RNC
(Radio Network Controller) as does a NodeB.
The operator, or carrier, network that interconnects all
of the base stations of the carrier is referred to as the evolved packet core (EPC) .
Traditionally, the core cellular network was circuit switched, but for 4G the core
is entirely packet switched. It is based on IP and supports voice connections using
voice over IP (VoIP).
Figure 10.10 illustrates the essential components of the EPC:
• Mobility management entity (MME): The MME deals with control signaling
related to mobility and security. The MME is responsible for the tracking and
the paging of UE in idle-mode.
• Serving gateway (SGW): The SGW deals with user data transmitted and
received by UEs in packet form, using IP. The Serving GW is the point of
interconnect between the radio side and the EPC. As its name indicates, this
gateway serves the UE by routing the incoming and outgoing IP packets. It is
the anchor point for the intra-LTE mobility (i.e., in case of handover between
eNodeBs). Thus packets can be routed from an eNodeB to an eNodeB in
another area via the SGW, and can also be routed to external networks such
as the Internet (via the PGW).
• Packet data network gateway (PGW): The PGW is the point of interconnect
between the EPC and the external IP networks such as the Internet.
The PGW routes packets to and from the external networks. It also performs
various functions such as IP address/IP prefix allocation and policy control
and charging.
• Home subscriber server (HSS): The HSS maintains a database that contains
user-related and subscriber-related information. It also provides support functions
in mobility management, call and session setup, user authentication, and
access authorization.
Figure 10.10 shows only a single instance of each configuration element. There
are, of course, multiple eNodeBs, and multiple instances of each of the EPC elements.
And there are many-to-many links between eNodeBs and MMEs, between
MMEs and SGWs, and between SGWs and PGWs.

## Slide 34
• Mobility management entity (MME): The MME deals with control signaling related to mobility and security. The MME is responsible for the tracking and the paging of UE in idle-mode.
• Serving gateway (SGW): The SGW deals with user data transmitted and received by UEs in packet form, using IP. The Serving GW is the point of interconnect between the radio side and the EPC. As its name indicates, this gateway serves the UE by routing the incoming and outgoing IP packets. It is the anchor point for the intra-LTE mobility (i.e., in case of handover between eNodeBs). Thus packets can be routed from an eNodeB to an eNodeB in another area via the SGW, and can also be routed to external networks such as the Internet (via the PGW).
• Packet data network gateway (PGW): The PGW is the point of interconnect between the EPC and the external IP networks such as the Internet. The PGW routes packets to and from the external networks. It also performs various functions such as IP address/IP prefix allocation and policy control and charging.
• Home subscriber server (HSS): The HSS maintains a database that contains user-related and subscriber-related information. It also provides support functions in mobility management, call and session setup, user authentication, and access authorization.

## Slide 35: Femtocells
A low-power, short range, self-contained base station
Term has expanded to encompass higher capacity units for enterprise, rural and metropolitan areas
By far the most numerous type of small cells
  operate in licensed and unlicensed spectrum that have a range of 10 m to several hundred meters.
Now outnumber macrocells
Key attributes include:
  IP backhaul
  Self-optimization
  Low power consumption
  Ease of deployment
Notes: Industry has responded to the increasing data transmission demands
from smartphones, tablets, and similar devices by the introduction of 3G and now
4G cellular networks. As demand continues to increase, it becomes increasingly difficult
to satisfy this requirement, particularly in densely populated areas and remote
rural areas. An essential component of the 4G strategy for satisfying demand is the
use of femtocells.
A femtocell is a low-power, short range, self-contained base station. Initially
used to describe consumer units intended for residential homes, the term has
expanded to encompass higher capacity units for enterprise, rural and metropolitan
areas. Key attributes include IP backhaul, self-optimization, low power
consumption, and ease of deployment. Femtocells are by far the most numerous
type of small cells. The term small cell is an umbrella term for low-powered radio
access nodes that operate in licensed and unlicensed spectrum that have a range
of 10 m to several hundred meters. These contrast with a typical mobile macrocell,
which might have a range of up to several tens of kilometers. Femtocells
now outnumber macrocells, and the proportion of femtocells in 4G networks is
expected to rise.

## Slide 36
Notes: Figure 10.11 shows the typical elements in a network that uses femtocells.
The femtocell access point is a small base station, much like a Wi-Fi hot spot base
station, placed in a residential, business, or public setting. It operates in the same
frequency band and with the same protocols as an ordinary cellular network base
station. Thus, a 4G smartphone or tablet can connect wirelessly with a 4G femtocell
with no change. The femtocell connects to the Internet, typically over a DSL,
fiber, or cable landline. Packetized traffic to and from the femtocell connects to the
cellular operator’s core packet network via a femtocell gateway.

## Slide 37: LTE-Advanced
Relies on two key technologies to achieve high data rates and spectral efficiency:
  Orthogonal frequency-division multiplexing (OFDM)
    Signals have a high peak-to-average power ratio (PAPR), requiring a linear power amplifier with overall low efficiency
  Multiple-input multiple-output (MIMO) antennas
Notes: LTE-Advanced relies on two key technologies to achieve high data rates and
spectral efficiency: orthogonal frequency-division multiplexing (OFDM) and
multiple-input multiple-output (MIMO) antennas. Both of these technologies are
explored in Chapter 17.
For the downlink, LTE-Advanced uses OFDMA and for the uplink SC-OFDM
(single-carrier OFDM).
OFDM signals have a high peak-to-average power ratio (PAPR), requiring
a linear power amplifier with overall low efficiency. This is a poor quality for battery-
operated handsets. While complex, SC-FDMA has a lower PAPR and is better
suited to portable implementation.

## Slide 38: Table 10. 3 Characteristics of TDD and FDD for LTE-Advanced
(Table can be found on
page 325 in textbook)
Notes: LTE-Advanced has been defined to accommodate both paired
spectrum for frequency-division duplex and unpaired spectrum for time-division
duplex operation. Both LTE TDD and LTE FDD are being widely deployed as each
form of the LTE standard has its own advantages and disadvantages. Table 10.3
compares key characteristics of the two approaches.

## Slide 39
The frequency offset, WO, used to separate the pair of channels
should be large enough for the user terminal to avoid self-interference
among the links because both links are simultaneously active.
Notes: FDD systems allocate different frequency bands for uplink and downlink transmissions.
The UL and DL channels are usually grouped into two blocks of contiguous
channels (paired spectrum) that are separated by a guard band of a number of vacant
radio frequency (RF) channels for interference avoidance. Figure 10.12a illustrates
a typical spectrum allocation in which user i is allocated a pair of channels Ui and Di
with bandwidths WU and WD . The frequency offset, WO, used to separate the pair
of channels should be large enough for the user terminal to avoid self-interference
among the links because both links are simultaneously active.
For TDD, the UL and DL transmissions operate in the same band but alternate
in the time domain. Capacity can be allocated more flexibly than with FDD. It
is a simple matter of changing the proportion of time devoted to UL and DL within
a given channel.

## Slide 40
Non-contiguous way: the multicarrier signal cannot be treated as a single signal and therefore multiple transceivers are required on UE.
Notes: Carrier aggregation is used in LTE-Advanced in order
to increase the bandwidth, and thereby increase the bit rates. Since it is important
to keep backward compatibility with LTE the aggregation is of LTE carriers.
Carrier aggregation can be used for both FDD and TDD. Each aggregated carrier
is referred to as a component carrier, CC. The component carrier can have a bandwidth
of 1.4, 3, 5, 10, 15, or 20 MHz and a maximum of five component carriers can
be aggregated, hence the maximum aggregated bandwidth is 100 MHz. In FDD,
the number of aggregated carriers can be different in DL and UL. However, the
number of UL component carriers is always equal to or lower than the number of
DL component carriers. The individual component carriers can also be of different
bandwidths. When TDD is used the number of CCs and the bandwidth of each CC
are the same for DL and UL.
Figure 10.13a illustrates how three carriers, each of which is suitable for a
3G station, are aggregated to form a wider bandwidth suitable for a 4G station.
As Figure 10.13b suggests, there are three approaches used in LTE-Advanced for
aggregation:
• Intra-band contiguous: This is the easiest form of LTE carrier aggregation
to implement. Here, the carriers are adjacent to each other. The aggregated
channel can be considered by the terminal as a single enlarged channel from
the RF viewpoint. In this instance, only one transceiver is required within the
subscriber station. The drawback of this method is the need to have a contiguous
spectrum band allocation.
• Intra-band noncontiguous: Multiple CCs belonging to the same band are used
in a noncontiguous manner. In this approach, the multicarrier signal cannot be
treated as a single signal and therefore multiple transceivers are required. This
adds significant complexity, particularly to the UE where space, power, and
cost are prime considerations. This approach is likely to be used in countries
where spectrum allocation is noncontiguous within a single band or when the
middle carriers are in use by other subscribers.
• Inter-band noncontiguous: This form of carrier aggregation uses different
bands. It will be of particular use because of the fragmentation of bands—
some of which are only 10 MHz wide. For the UE it requires the use of
multiple transceivers within the single item, with the usual impact on cost,
performance, and power.

## Slide 41: Summary
Principles of cellular networks
  Cellular network organization
  Operation of cellular systems
  Mobile radio propagation effects
  Fading in the mobile environment
Cellular network generations
  First generation
  Second generation
  Third generation
  Fourth generation
LTE-Advanced
  Architecture
  Transmission characteristics
Notes: Chapter 10 summary.