## Slide 1: Internet of Things A New Frontier of Multimedia Research
Kien A. Hua
Department of Computer Science
University of Central Florida

## Slide 2: Three Topics
Sending emails
Web browsing
Video Streaming
Internet of Things (IoT)
Stress on Internet
On-demand streaming will make up 82% of Internet traffic by 2021
Continuous streaming from billions of Internet of things can be even more demanding
time
Where do we get network bandwidth for IoT ?
82%
100%
2021

## Slide 3: Three Topics
Sending emails
Web browsing
Video Streaming
Internet of Things (IoT)
Stress on Internet
On-demand streaming will make up 82% of Internet traffic by 2021
Continuous streaming from billions of Internet of things can be even more demanding
time
DON
1
ThingStore
2
Tabletop
3
Future workplaces with human-things teaming
82%
100%

## Slide 4
Deduplication Overlay Network (DON)

## Slide 5
Video Dominating Internet
Even with caching, CDN, P2P, proxies, multicast streaming, etc., there is still a need to improve video streaming
72%
2016
75%
2017
77%
2018
79%
2019
80%
2020
82%
2021

## Slide 6
Conventional Wisdom
Traffic congestion
is bad for networks
Routing algorithms have been designed to avoid congestion

## Slide 7
Traffic congestion
is bad for networks
today ?
… Is this
still true
Conventional Wisdom
What if we can turn congestion into advantage ?

## Slide 8: Communication Patterns Change …
PAST: One-to-one communication
Congestion is bad !!
TODAY: One-to-many communication
Congestion is still bad ?

## Slide 9
Video Traffic Is Different
Just 5% of the videos account for 95% of total views at YouTube
80:20 rule also applies to video streaming
Majority of people watch the new movie releases
One-to-MANY communication

## Slide 10
New Pattern New Solution
An idea: Video Streaming Tree
A lot of “duplicated” video traffic
Moving the duplicated traffic off the network helps, how ?
Since 80:20 rule also applies to video streaming

## Slide 11
S1
S1
Deduplication router
Stream S1 begins
Dynamic Stream Merging
Staging buffer
Packet P1
Can also be a video segment

## Slide 12
S1
S1
Stream S2 begins
S2
S2
Dynamic Stream Merging
Packet P100
Packet P1

## Slide 13
S1
S1
Stream S1 is recorded in preparation for merge
S2
S2
Packet P150
Packet P100
Dynamic Stream Merging
Packet P50

## Slide 14
S1
S1
S2
Packet P100
Packet P200
Saving bandwidth
Dynamic Stream Merging
S2
In this example, s2 is merged with s1 : (s1 → s2)
80:20 Rule - we can have s1 → s2 → s3 → … → sk and save k-1 streams
Stream S2 is blocked and merge begins

## Slide 15
S1
S1
S2
Packet P100
Packet P200
Saving bandwidth
Dynamic Stream Merging
S2
In this example, s2 is merged with s1 : (s1 → s2)
80:20 Rule - we can have s1 → s2 → s3 → … → sk and save k-1 streams
Move redundant traffic off the network
Turn congestion into advantage

## Slide 16
Deduplication routers
Video Streaming Tree

## Slide 17
Merge
Video Streaming Tree

## Slide 18
Merging taking place independently throughout the network incrementally constructs a video streaming tree – An opportunistic approach
Video Streaming Tree

## Slide 19
Video Streaming Tree
Merging taking place independently throughout the network incrementally constructs a video streaming tree – An opportunistic approach

## Slide 20
Video Streaming Tree
Merging taking place independently throughout the network incrementally constructs a video streaming tree – An opportunistic approach

## Slide 21
Controlling redundancy prevents bottlenecks and reduces network traffic
More traffic
Without deduplication
Congested with “redundant” traffic
Video Streaming Tree
With deduplication
Substantial traffic reduction

## Slide 22
Multicast Tree ≠ Streaming Tree
Multicast tree: Wait for multicast time
→ Not on demand
Server
Streaming Tree: zero delay
→ Video on demand
Server

## Slide 23: Deduplication Overlay Network
Deduplication Overlay Network (DON) consists of deduplication routers capable of merging ‘duplicate’ video streams
DON reduces traffic for the underlying network
DON (Deduplication Overlay Network)
Deduplicationrouter
Logical link
Underlying network
Physical link
Conventional router

## Slide 24: DON Experiment
A line topology with DON routers in Florida, South Carolina, North Carolina, Washington D.C., and New York
PlanetLab Servers as DON routers

## Slide 25: A Wireless Setup
Limited number of mesh nodes available
Link 1
Link 2
Link 3
Link 4
Mesh gateway connected to campus network through Ethernet
Line-mesh topology allows us to maximize the number of hops (typically encountered in larger mesh networks)
Notes: There are n+1 users. One of them requests video x , and all the other users request video y at different times. These users are randomly placed among nodes n2 , n3 , and n4 .

## Slide 26: Video Stream Performance
More congestion, video x becomes unwatchable
One request for video x
Increasing requests for video y (more congestion)
With stream merging, video x continues to perform well
Congestion impact on video X

## Slide 27: Stress Test on Network Links
20 requests for the same video
Plot shows accumulated data transmitted at each link
Without merging: (1) More traffic (2) Routers near gateway completely saturated
With merging: (1) Nodes near gateway are not saturated (2) Supporting more than 20 video requests is possible
Without merging
With merging

## Slide 28
Merger-Aware Routing
Conventional routing algorithms are designed to reduce congestion by distributing load
We want to combine the load to increase merging opportunity
 A merger-aware routing technique is helpful
The server uses less time to transmit 25 streams of the video
Notes: In “No Merge,” the server takes the same amount of time to transmit the video 25 times regardless of the level of concurrency among these streams (i.e.,the same amount of total data need to be transmitted). With merging, the server needs to send less data for the 25 clients. With merging, the clients can receive data “originated” from many routers beside the server. As a result, the reduction in the server-transmitting data decreases with increases in the level of concurrency.
The simulation time is shorter for the case with a higher concurrency. Each simulation runs until all 25 streams are done. The level of concurrency is controlled by the video request rare.

## Slide 29
ThingStore
Collaboration in IoT Development and Deployment
ThingStore

## Slide 30: Today’s Internet Users
This is changing

## Slide 31
“Things” are connected devices
INTERNET
Alert !
New Internet Users: “Things”
Regular cameras, thermal cameras, microphones, and a variety of sensors

## Slide 32
There will be 28 billion “things” by 2020
Sensing environment
Transmitting data
“Things” are good helpers
The Internet of Things (IoT)
Gartner, Inc.

## Slide 33
There will be 28 billion “things” by 2020
Gartner, Inc.
Biggest big data ever !!!
The Internet of Things (IoT)

## Slide 34: Big Data and Cloud Computing
Big data are at data center, ready for cloud computing

## Slide 35: IoT Is a Different Kind of Big Data

## Slide 36: IoT Is a Different Kind of Big Data
Potentially billions of live data sources continuously feeding from all across the Internet in real time
Cloud Computing
IoT data source
1st IoT Challenge
Communication is potentially a serious bottleneck
1
Conventional Big Data

## Slide 37
Event notification
End users
IoT App
Any kind of sensor
Any kind of camera
IoT Challenge #2
‘Thing’ heterogeneity
Software development is complex
2
Today Focus in
Big Data research
Notes: From KSC slides

## Slide 38
Event notification
End users
IoT App
IoT App
IoT App
Any kind of sensor
Any kind of camera
No standard for IoT application development
How to share IoT infrastructure ?
3
IoT Challenge #3
Notes: From KSC slides

## Slide 39
ThingStore
Addresses These Challenges
Avoids flooding the Internet
Simplifies software development
Enables sharing of IoT Infrastructure

## Slide 40
‘Things’ in ThingStore
Thing Server
S1
S1
S1
S1
S1
S2
Deploy “things” with smart services
Internet of Things are made intelligent with event detection software, smart services
Smart services carry out computations upon raw data generated by their physically collocated or decoupled sensing components
Thing Provider
Smart services

## Slide 41
Thing Server
S1
S1
S1
S1
S1
S2
Deploy “things” with smart services
Thing Provider
Simulated live camera view
Smoke detected by smart service
(color coded)
S2
Smart Service Example
Camera
A smart service of the camera
“1”
Other smart services of the camera

## Slide 42
Thing Server
S1
S1
S1
S1
S1
S2
Deploy “things” with smart services
Thing Provider
Smart Service
Smart services transform raw data into meaningful information
Development of smart services (thing operators) is left to Thing experts
I have a PhD in multimedia computing

## Slide 43
S4
S3
S2
S1
Thing
4 smart services
Any kind of Camera
S6
S5
S4
Thing
3 smart services
Any kind of sensor
0
0
1
0
1
1
0
0
0
1
1
1
0
0
0
0
1
1
0
0
0
0
0
1
1
1
0
0
3
2
1
Applications
0
1
1
0
0
1
0
0
0
0
1
1
0
0
1
0
1
1
0
0
1
EQL Processor
(Boolean Query Processing)
Atomic events
Complex events
System Overview

## Slide 44
S4
S3
S2
S1
Thing
S6
S5
S4
Thing
0
0
1
0
1
1
0
0
0
1
1
1
0
0
0
0
1
1
0
0
0
0
0
1
1
1
0
0
3
2
1
Applications
0
1
1
0
0
1
0
0
0
0
1
1
0
0
1
0
1
1
0
0
1
EQL Processor
(Boolean Query Processing)
A programming interface for sharing IoT Infrastructure
Edge computing → No need to stream raw data
Addressing Challenges
Boolean abstraction hides complexity due to device heterogeneity
1
2
3
App Developers only focus on the application logic
Thing servers at the “edge” of network
Challenge
Challenge
Challenge
This runs counter to the theme of consolidation and massive data centers that has dominated the discourse on cloud computing.

## Slide 45
EQL Example
Internet
  SELECT event-handler
  FROM Thing1 T1
  WHEN Before(T1.S3, T1.S1)
  WITHIN 30 seconds
  UNTIL 60 minutes
Computer program
Event specification
IoT App
IoT App
IoT App
S1
S1
S1
S1
S1
S2
EQL query
EQL query
EQL query
1
0
0
1
1
0
0
0
Event notification
End users
Termination Clause:
UNTIL time
UNTIL true
UNTIL forever
T1
T2
Notes: From KSC slides

## Slide 46
Event Evidence
App may request event evidence for further processing
App
Thing Server
…
Query
“1”
Evidence ?
Raw data
Optional
Further analysis
Event handling

## Slide 47
EQL vs SQL
SQL: Value-based search
EQL: Event-based search
Search
Search

## Slide 48
T7.S1
T1.S3
T7.S4
T1.S2
Before
Meets
And
S4
S3
S2
S1
Thing1
S6
S4
S2
S1
Thing7
EQL Query Processing
Multimedia Computing
Processing “WHEN” clause in EQL - Asynchronous Data stream processing
Boolean abstraction as a framework for multimedia data stream processing
Notes: <click>
For query processing, event states are sampled in discrete time intervals and dynamic tables are created.
<click>
Logical and temporal query operations are performed on dynamic event tables.

## Slide 49
Ad Hoc EQL Query
  SELECT event-handler
  FROM Thing1 T1
  WHEN Before(T1.S3, T1.S1)
  WITHIN 30 seconds
  UNTIL 60 minutes
S1
S1
S1
S1
S1
S2
1
0
0
1
1
0
0
0
Event-handling software
Notification
Atomic event
Complex event
New observation
Notes: From KSC slides

## Slide 50
Embedded EQL
  SELECT [event-handler]
  FROM Thing1 T1
  WHEN Before(T1.S3, T1.S1)
  WITHIN 30 seconds
  UNTIL 60 minutes
S1
S1
S1
S1
S1
S2
1
0
0
1
1
0
0
0
Computer program
Call callback entry
Control command
Notes: From KSC slides

## Slide 51
ThingStore
Network
Thing Server
S1
S1
S1
S1
S1
S2
Deploy “things” with smart services
Thing Provider
IoT Market Place
ThingStore
S1
S1
S1
S1
S1
S2
An Ecosystem for IoT Collaboration

## Slide 52
Develop apps as online services
IoT App Developer
app
App Server
app
app
IoT Market Place
ThingStore
app
app
app
app
S1
S1
S1
S1
S1
S2
Download
Network
End Users
Subscription
Thing Server
S1
S1
S1
S1
S1
S2
Deploy “things” with smart services
Thing Provider
Query Processor
EQL queries
An Ecosystem for IoT Collaboration
ThingStore

## Slide 53
Develop apps as online services
app
App Server
app
app
IoT Market Place
ThingStore
app
app
app
app
S1
S1
S1
S1
S1
S2
Thing Server
S1
S1
S1
S1
S1
S2
Deploy “things” with smart services
Query Processor
Cloud Computing
Edge Computing
Deployed at data center
Deployed at the edge
Leverage both parallel and distributed processing
ThingStore

## Slide 54: Query Optimization Computation Sharing: Merging Queries
Before
S4
A new query
S3
Execution Pool
Before
AND
S1
S2
S3
Join
Duplicate computation
A forest of query trees

## Slide 55: Computation Sharing
Execution Pool
Before
AND
S1
S2
S3
Buffer
Before
S4
New query
Computation sharing
After
S3
A new query
S2
Join ?

## Slide 56: Query Optimization
Query 34
Query 22
Query 16
Waiting Queue
Translator
O4
O5
O3
O6
O2
O1
O4
O5
O3
O6
O2
O1
O4
O5
O3
O6
O2
O1
Execution Plans
EX1
EX3
EX2
Execution Pools (multithreaded)
Optimizer
Optimized queries for EX1
Optimized queries for EX2
Optimized queries for EX3
Query Results
These queries share computation performed by executor EX3

## Slide 57
Collaboration platform for IoT development and deployment
ThingStore
An Ecosystem for IoT Collaboration
Thing Developer
IoT App Developer
IoT Users

## Slide 58
Working with ‘Things’
Future Workplaces

## Slide 59: Today’s Workplaces
Most people collaborate using emails

## Slide 60: Future Workplace
Human-Things Teaming

## Slide 61: Future Workplaces with IoT
Fusing human and machine intelligence opening up a host of new opportunities

## Slide 62: Collaborating with ‘Things’
Challenge: Human teams need to be much more efficient
Information overload

## Slide 63: TABLETOP
A Multimedia virtual meeting room for time critical decision making

## Slide 64: Sharing Desktop Objects
Desktop
Private space
Tabletop
Collaboration space
Seamless interoperability of Tabletop and Windows Desktop enables fast access and sharing of private and Internet information in meetings
Browser
The “world”

## Slide 65: Sharing the Internet of Things
Users can co-operate on ‘things’ during a meeting
My IoT folder
Containing IoT bookmarks

## Slide 66
S1
S1
S1
S1
S1
S2
New observation
IoT Applications
Network
Event Notification
Command
Domain expert
Operator
Human-Things
collaboration
Tabletop collaboration
Thing Server
Command
Future Workplace with human-machine teaming

## Slide 67: Tabletop

## Slide 68
Summary
DON - Turning Traffic Congestion into Advantage
1
2. ThingStore - An ecosystem for IoT Development and Deployment
2
Tabletop - Collaboration in Future IoT Workplaces
3

## Slide 69
kienhua@cs.ucf.edu

## Slide 70
Some Related Publications
Kutalmis Akpinar, Trevor Ballard, Kien A. Hua, Kai Li, Sansiri Tarnpradab, and Jun Ye, “COMMIT: A Multimedia Collaboration System for Future Workplaces with the Internet of Things,” in Proc. ACM International Conference on Multimedia Systems, Taipei, June 20-23, 2017.
Kutalmis Akpinar and Kien A. Hua, “ThingStore - An Internet of Things Management System,” in Proc. of IEEE Int’l Conference on Multimedia Big Data, Laguna Hills, California, April 19-21, 2017.
Kutalmis Akpinar, Kien A. Hua, and Kai Li, “ThingStore: A Platform for Internet-of-Things Application Development and Deployment,” in Proc. of 9th ACM International Conference on Distributed Event-based Systems, Oslo, Norway, June 29 – July 3, 2015.
Kien A. Hua, Ning Jiang, Jason Kuhns, Vaithiyanathan Sundaram, and Cliff Zou, “Redundancy Control through Traffic Deduplication,” in Proc. of Infocom 2015, April 26 – May 1, 2015.
DON
ThingStore
Tabletop
Kutalmis Akpinar, Fereshteh Jafariakinabad, Kien A. Hua, Omar Nakhila, Jun Ye, and Cliff Zou, “Fault-Tolerant Network-Server Architecture for Time-Critical Web Applications,” in Proceedings of IEEE International Conference on Dependable, Autonomic and Secure Computing, Orlando, November 6-10, 2017.
Kutalmis Akpinar and Kien A. Hua, “Deduplication Overlay Network,” in Proceedings of IEEE International Symposium on Network Computing and Applications, Cambridge, October 30 – November 1, 2017.