## Slide 1
Kien A. Hua
Department of Computer Science
University of Central Florida
Mobile Data Collection Networks for Wireless Sensor Networks

## Slide 2: Wireless Sensor Network (WSN)
Wireless Sensor Network is composed of a large number of wireless sensors
Wireless sensors are
  small size, low cost, low power, and irreplaceable in many applications
  normally distributed in an ad hoc manner
These sensors gather information, such as pressure, humidity, temperature, speed etc.

## Slide 3: Many Applications
Rescue Operations
  Damage assessment, fire monitoring, radiation detection, chemical sensing
Environment
  Forest fire detection, water quality assessment, habitat monitoring
Health applications
  Patients monitoring, drug administration
Industry
  Production temperature, humidity, pressure control

## Slide 4: Traditional Wireless Sensor Network
Internet
Wireless Sensor
Sink/Base Station
  Sensing data routed to sink or base-station (sometimes further transmitted over the Internet) for further analysis or applications.
  Data generated at each sensor can only reach their neighbors within communication range
  Data go through multiple sensors on their way to the sink

## Slide 5: Data Collection Issues
Sink/Base Station
Wireless Sensor
Multi-hop communication: a major limitation for these energy-constrained sensors
Energy hole problem: Sensors near the sink deplete their energy faster. This renders the WSN inoperable prematurely
Notes: Sensors assume dual roles: data source and data forwarder

## Slide 6: Some Solutions
Adding mobile elements is considered a promising solution to reduce sensor energy consumption
Two approaches
  Mobile Sink Approach
  Mobile Messenger Approach

## Slide 7: Mobile Sink Approach
Mobile Sink
Sinks moves to different locations in the network field during WSN lifetime
Sojourn for a time interval at each location
When sojourning, routing path of sensors are updated and traffic is redirected towards the current sink location

## Slide 8: Mobile Sink Approach
Advantages
  The “neighborhood” of the sink change for each new sink position
    Distribute burden of data forwarding over the whole network
    Prevent premature cessation of network operation.
Limitations
  Sensors still do multi-hop communication
  Mobile sink is not feasible for some applications (e.g. it might not be possible to have access to Internet at some of the positions in a harsh environment)
  Not scalable for large-scale WSNs

## Slide 9: Mobile Messenger Approach
Sink
Mobile Messenger
Sinks are static
Mobile messengers start out from the sink site, following a path, to visit each sensor
Sensors upload their data to the messenger (in a single hop) when they approach.
Mobile messengers go back to the sink to deliver the collected data

## Slide 10: Mobile Messenger Approach
Advantages
  Sensors transmit data in a single hop, and do not forward data for other sensors
    Less communication overhead w.r.t. routing
    Energy consumption at each sensor greatly reduced
Limitations
  Sensors have to wait for the messenger to approach, resulting in long or unpredictable latency
  long waits may cause sensor buffer overflows, reducing data delivery ratio
  Adding mobile messengers reduces average wait time; however they quickly increase the cost of the system

## Slide 11: Another Data Collection Paradigm
MDCNet - Mobile Data Collection Network
Mobile Relay Node: service load adjusted to achieve desired performance
Sensor: one-hop communications → energy efficient
Electronic data transmission → low latency, high data delivery ratio
1
2
3

## Slide 12: MDCNet – Approach
Approach: MDCNet is a wireless mesh network with virtual mesh nodes
  Sensors are clustered into groups, each serviced by a virtual mesh node
  Sensors communicate with their designated virtual mesh node through single-hop communications
  Through the mesh nodes, sensors can upload data and electronically transmit them towards the sink(s)
What is a virtual mesh node ?
Connected only when data transmission is needed
Intermittent connection
Virtual mesh node

## Slide 13: Mobile Mesh Nodes (Relay Nodes)
Land-based:
mini autonomous vehicle
Airborne: quadricopter
Underwater:
mini communication satellite

## Slide 14: MDCNet – Challenges
MDCNet (i.e., the virtual mesh nodes) must be self-deployed
Need a data collection protocol
Need a data forwarding protocol
What is a virtual mesh node ?
Intermittent connection
Virtual mesh node
Connected only when data transmission is needed

## Slide 15: MDCNet – Design Considerations
Each MRN should serve about the same number of sensors to reduce sensor contention
Sensor’s data should be collected in a timely manner to avoid data loss caused by sensor buffer overflows
Data relay among MRNs should conform to a reliable protocol to guarantee safe arrival at the sink

## Slide 16: MDCNet Self-deployment Techniques
Deterministic Area Partitioning (DAP) Scheme
Adaptive Search & Conquer (ASC) Scheme

## Slide 17: Self-Deployment: DAP Scheme
Assumption
  Sensors are uniformly distributed over the sensing field
Deployment strategy
  Evenly divide the region into equal partitions
  Associate each partition with a mobile relay node
  MRN moves back and forth in a snake-like pattern to collect data from sensors
R: Wireless communication range

## Slide 18: Self-Deployment: ASC Scheme
Adaptive Search and Conquer (ASC) approach has the following characteristics
It assumes no knowledge of sensor distribution
MRNs cooperatively and incrementally search and conquer different regions until the whole WSN has been covered, i.e., self deployment

## Slide 19
L+2·R
L+2·R
1
2
3
Self-Deployment: ASC Scheme
4th expansion by 2·R
2nd expansion by 2·R
3rd expansion by 2·R
1st expansion by 2·R
After claiming the service area, the MRN moves in a snake-like pattern to collect data from the sensors
MRNs set a random timer. The MRNs whose timer expire first start out to claim the next service areas.
These target areas are explored in parallel
Notes: MTNs set a random timer in the beginning, the MRN whose timer expires first will be the first to start out, and at the same time send out a TIMEOUT message. Other MRNs will cancel their timer upon receipt of this message.
The other three target areas will be explored by other MRNs upon their receipt of the NOTICE message from the MRN that claimed the bottom-left region.

## Slide 20: ASC Search Hierarchy
1
4
2
3
8
5
6
7
9
Sink
1
2
8
6
7
3
9
5
4
Regions are explored in parallel in a hierarchical manner
O(Sink Location)

## Slide 21: ASC Search Hierarchy
1
4
2
3
8
5
6
7
9
Sink
1
2
8
6
7
3
9
5
4
O(Sink Location)
A
1
1
1
C
1
1
B
Regions are explored in parallel in a hierarchical manner

## Slide 22: Data Collection Protocol
Move& broadcast
If satisfy service requirement, set a wait timer and wait for data
The sensor has not received service within a predefined time period. (This is to make sure that a sensor does not get repetitive service when MRN is within its communication range )
Mobile Relay Node
Sensor
time
4. Start sending data packet
.
.
.
1. HELLO message
2. ACK message
3. START message
5. FINISH message
Cancel timer & receive data
End Session
Timeout if sensor still has not started data transmission
Data not coming

## Slide 23: DAP: Data Relay Hierarchy
O(Sink Location)
1
2
3
6
5
4
8
7
9
1
5
4
2
7
8
6
6
3
Sink
Parent node is the neighbor node closest to the sink

## Slide 24: DAP: Data Relay Hierarchy
O(Sink Location)
1
2
3
6
5
4
8
7
9
1
5
4
2
7
8
6
6
3
Sink
Nodes 2 and 4 communicate directly with sink if they are within the radio range

## Slide 25: DAP: Data Relay Hierarchy
O(Sink Location)
1
2
3
6
5
4
8
7
9
1
5
4
2
7
8
6
6
3
Sink
MRNs form a mesh network with intermittent connections between the mobile mesh nodes

## Slide 26: ASC: Data Relay Hierarchy
The data relay hierarchy is the same as the search hierarchy
1
4
2
3
8
5
6
7
9
Sink
O(Sink Location)
1
2
8
6
7
3
9
5
4
Communicate directly with sink if node 3 within radio range

## Slide 27: Data Relay Protocol
MRN (child)
time
.
.
.
HELP message
Ready message
Stop serving sensors and set a wait timer
start sending data packet
Cancel timer & receive data
Stop serving & seek help
MRN (parent)
FINISH message
Resume serving sensors
Session ends
Transmit data
Serving sensors
Timeout
Serving sensors
Data not coming

## Slide 28: Simulation Study
Environment: NS2
Sensing Area: 100m х 100m
Sensor Nodes
  data generation rate: 10bit every 0.1 seconds
  buffer capacity: 10KB
  communication radius: 7m
  random distribution
Mobile Relay Nodes
  moving speed: 2m/s
  communication radius: 40m

## Slide 29: Performance Metrics
Data delivery ratio
  Percentage of data packets delivered to the sink
Latency
  Average service interval by mobile relay nodes
  Deployment time (for ASC approach)
  Total search time of mobile relay nodes

## Slide 30: Placement of Sensors
1
2
3
4
5
6
7
8
9
10
12
15
16
18
20
11
13
14
17
19
21
22
23
24
26
27
25
28
29
30
31
32
33
34
35
36
37
38
Number of sensors are evenly divided among the cells
Sensors are randomly placed within their own cell

## Slide 31: Area Fragmentation
Target Area for 3rd Round
Determined in 2nd round
Determined in 1st round

## Slide 32: Effect of Sensor Density
DAP 4 MRNs are enough for the spatial coverage of the application terrain. Increases in number of sensors increases the load for each MRN.
ASC keeps the workload at 50 sensors per MRN, and adjusts the sizes of the service areas accordingly. Using more sensors requires more MRNs
When there are less than 300 sensors, MRNs have not reach full load. Thus, 300 is the full load point for our setting
When sensors are very sparse, It takes the 1st MRN a long time to discover its service area, which dominates the deployment time
As sensors density increases, more MRNs are dispatched, which contributes to the gradual increase in deployment time
DAP: 4 MRNs
ASC: 50 sensors per MRNs
With more sensors, it takes less time to deploy the first MRN
MRNs experiencing increasingly higher load
Increasing in number of MRNs reduces the latency
Notes: ASC Deployment: 50 sensors per MRN. Add more MRNs for more sensors. When the number of sensors is very low, only a small number of MRNs is needed. However, they have a larger service area resulting in less than optimal performance (lower delivery ratio).
ASC: Increasing in the number of MRNs reduce the service area for each node. This helps to reduce the latency.

## Slide 33: Effect of Load factor (ASC approach)
When load factor exceeds 60, the number of partitions can not decrease any more given the number of sensors (i.e. at least 4 parts)
Taking all factors (latency, data delivery ratio, cost in terms of number of MRNs needed) into account, the optimal load factor in our setting should be between 40 to 50.
Too many sensors per MRN. They are overloaded
Latency shows rapid increase around 50, as a result of overload
1
2
3
4
performance does not degrade anymore, because partition number has reached minimum
Notes: We need 11 MRNs for both 20 and 30 load factors. This is due to rectangular shape of each monitoring subregion. A subregion might have slightly more sensors than the specified load factor if the MRN has found “enough” sensors before it reaches the end of the current row or column of the rectangular monitoring region.

## Slide 34: Conclusion and Future Work
A Mobile Data Collection Network (MDCNet) is a wireless mesh network with intermittent connections between mobile mesh nodes
MDCNet has a number of advantages
  Single-hop communication saves sensors energy
  Electronic transmission of sensing data (instead of carried by messenger nodes) results in shorter latency
  It is self-deployed and capable of preventing network partitions
Room for Improvement
  Self-deployment techniques that do not require mobile relay nodes with GPSs are desirable
  Generalization to irregular-shaped service areas
  Consideration of obstacles and/or constrained paths

## Slide 35
kienhua@cs.ucf.edu