## Slide 1: Computer Architecture
Lecture 3
Bus Architectures

## Slide 2: Bus(es)
A bus is a hardware channel through which information can flow between components connected to the bus.
It allows us to simplify our current model and to make further additions more easily.
Only two components may communicate through a bus at any given time.

## Slide 3: One Bus Design
Memory
MDR
MAR
A
IP
BUS
1
Decoder
ADD
ALU
IR
OP
ADDR
C

## Slide 4: Instruction Set
Fetch(00)
MAR <- BUS<-PC
MDR <- Memory[MAR] || PC <-PC + 1
IR <-BUS<-MDR
Decoder <- IR.Opcode
MAR<-BUS<-IR.ADDR
Store(01)
MDR<-BUS<-A
Memory[MAR]<- MDR
Load(02)
MDR <-Memory[MAR]
A <-BUS<-MDR
ADD(03)
MDR <-Memory[MAR]
C <- A + MDR (ALU<-BUS<-MDR)
A<-BUS<- C
END(04)
Stop
JMP (05)
PC  IR.ADDR

## Slide 5: Two Bus Design(modify)
Memory
MDR
MAR
A
IP
BUS 1
1
Decoder
ADD
ALU
IR
OP
ADDR
BUS 2

## Slide 6: 2 Bus Design
With the added bus, 2 pairs of components may communicate in parallel.
The additional bus does not change the current instruction set.
Extra registers maybe need to allow data to be transferred from one bus to the other. In this example registers A, IP, and IR are used for this function.

## Slide 7: 2-BUS Architecture
A
ALU
OP ADDR
PC
M
E
M
O
R
Y
4
MDR
MAR
B
C
+
Decoder

## Slide 8: Instruction Formats
The Format of the current instructions are OP <ADDR>
To provide instructions of the format
ADD, R1, R2, R3
and
STORE R3, <ADDR>
where R1, R2 and R3 are registers we need to add an architecture to select the appropriate register

## Slide 9: Register File
By utilizing a register file you can organize the registers in one array
The control unit allows us to select the appropriate register for the operation and load it into its target location (either memory or another register)
This is a crucial aspect of the Load/Store architecture

## Slide 10: One Bus with Register File Load/Store Instruction Format
Memory
MDR
MAR
A
r3 ADRR
IP
BUS
Decoder
ALU
C
Register File
r1
r2
r3
r4
OP
Select register
OP
R
<ADDR>
10
12
0
15
11
9

## Slide 11: One Bus with Register File Register to Register Format
Memory
MDR
MAR
A
r3 r1
IP
BUS
Decoder
ALU
C
Register File
r1
r2
r3
r4
OP
Select register
OP
R
No used
10
12
0
15
11
9
8
R

## Slide 12: 2-BUS Load/Store Architecture with Register File
A
ALU
OP
PC
M
E
M
O
R
Y
4
MDR
MAR
Register File

## Slide 13: Instruction Formats
The instruction format must be modified
Three instruction formats are used
OP
<ADDR>
OP
R2
R1
OP
R
<ADDR>
R3
12
0
10
12
12
0
0
8
4
15
15
15
11
11
7
11
3
9

## Slide 14: 3-BUS Load/Store Architecture with Register File
By adding a third BUS the system can load two registers at once using each BUS
Two multiplexers need to be attached to the output of the register file: one connected to each BUS to send the contents of the target register to its destination
Another multiplexer unit is added to send input from the third BUS into the correct location within the register file

## Slide 15: 3-BUS Load/Store Architecture with Register File
ALU
OP
PC
M
E
M
O
R
Y
4
MDR
MAR
Register File

## Slide 16: Control Unit
Decoder
PC
MAR
MDR
IR
T1
T2
T3
M
T4
T5
OP ………..

## Slide 17: Clock Unit
The Latch will only allow the change of the value on each clock tick
By linking as a ring counter we create a clock distributor
D
Q
0
D
Q
D
Q
1
T1
T2
T3
0

## Slide 18: Clock Unit
At every clock tick the active flip-flop changes, sending a signal to execute a different step of the current instruction in turn
D
Q
0
D
Q
D
Q
1
0
D
Q
1
D
Q
D
Q
0
0
D
Q
0
D
Q
D
Q
0
T1
T2
T3
1
T1
T2
T3
T1
T2
T3

## Slide 19: Control Unit
OP ………..
PC
MAR
MDR
IR
T1
T2
T3
M
T4
T5
Decoder
Each line emerging from the decoder represents an operation. When the decoder is set to that operation, it sends voltage down the appropriate channel which is ANDed with the signals coming from the clock. This allows for precise timing in the step executions of instructions and makes synchronization among components possible.

## Slide 20: Control Unit
OP ………..
PC
MAR
MDR
IR
T1
T2
T3
Fetch Cycle:
T1: MAR <- PC
T2: MDR <- M[MAR]
T3: IR <- MDR
T4: MAR <- IR.ADDR
T5: Decoder <- IR.OP
The chain of flip-flops will be
as long in clock ticks as the
longest command takes to
execute.
M
T4
T5
Decoder

## Slide 21: One-Address Format
The operation is 4 bits and the remaining 12 are address bits
This gives the availability of 2 4 operations and 2 12 memory locations
OP
<ADDR>
12
0
15
11

## Slide 22: One-Address Format
0000 is the Fetch operation(hidden instruction)
It is a hidden instruction that cannot be accessed by the user
OP
<ADDR>
12
0
15
11
15-12
0000
0001
0010
0011
…
1111
Fetch
Add
Command
Sub
Mult

## Slide 23: Two-Address Format
The operation is performed on the memory addresses of the first and second operands and the value is stored back in the location specified by the first operand field
OP
1st Operand/
Result
2nd Operand
12
0
5
15
11
6

## Slide 24: Two-Address Format
100
200
CPU
Add
200
100
12
0
5
15
11
6
This is analogous to:
Load 200
Add 100
Store 200
all performed in one command

## Slide 25: Three-Address Format
The operation is performed on the memory addresses of the first and second operands and the value is stored in the location specified by the result address field
OP
1st Operand
Result
2nd Operand
12
0
8
4
15
11
7
3
This format is not often used because
it requires three memory accesses per
operation (which is very slow)

## Slide 26: Three-Address Format
100
200
300
CPU
Add
200
300
100
12
0
8
4
15
11
7
3
This is analogous to:
Load 200
Add 100
Store 300
all performed in one command

## Slide 27: Another Three-Address Format
R1
R2
R3
CPU
Add
R2
R3
R1
12
0
8
4
15
11
7
3
In a Load/Store machine, the addresses are often locations in the register file rather than in memory. This is very fast on a machine with multiple-BUS architecture.