## Slide 1: Proposed framework for NFC IDS/IPS
CAP 6135 – Spring 2011
Sharif Hassan
Leith Tussing

## Slide 2: Topics
RFID Information
NFC Description
Security Threats
NFC IDS/IPS
References

## Slide 3: NFC ~ RFID
NFC utilizes RFID but what is RFID?
  Radio Frequency IDentification
    RFID Tag CPU
    Radio Receiver
    Radio Modulator
    Control Logic
    Memory
    Power System
  RFID Tag Antenna
    Input & Output
  RFID Reader/Writer
Notes: RFID as a technology has existed since 1915 but was not fully used until WWII as a means for tracking allied bombers during night time raids.
All RFID systems consist of the items listed.
  RFID Tag CPU – Computation controller to perform basic to complex math depending on the complexity of the design.
  Radio Receiver
  Radio Modulator
  Control Logic
  Memory – Depending on the system some are locked ROMs while others have writeable memory allowing them to be reprogrammed remotely.
  Power System – There are two types of RFID power systems, passive which use only the power provided to them from the RF signal, and active which require some sort of power source either via a battery or power line to provide boosted signal strength and/or processing power.
  I/O Antenna – The different RFID systems due to the way RF signals work require unique antennas to provide signal acquisition for the varying frequency ranges. Lower frequencies will require larger antenna systems where the high, and ultra-high can operate with smaller designs.

## Slide 4
Notes: UHF (Ultra High Frequency 860 MHz ~960 MHz) based toll collection sticker. Allows full speed reading at up to 100 mph and 10 meters.
LF (Low Frequency 125 KHz) RFID tokens and Proximity Cards. Extremely short range with a maximum range of 10 cm and a very small data payload.
ISM (Industrial, Science, & Medical 2.4 GHz) tracking bracelets originally designed for medical facilities. Allows real time tracking with advanced systems with a range of up to 100 m of up to 300 tags.
HF (High Frequency 13,56 MHz) Casino chips used to prevent counterfeit chips as well as patron tracking.
Hitachi Global mu-chip 0.04mm * 0.04mm is the worlds smallest RFID chip. The black line is a human hair with several tags around it. These devices operate at the ISM 2.4 GHz frequency with a range of 25 cm and a storage capacity of 128-bit.
Global e-Passport using the HF 13.56 MHz and after initial hiccups is the best example of high RFID security.
  Faraday cage in the lining to prevent being read when the cover is closed
  Basic Access Control (BAC) in the form of a Machine Readable Zone (MRZ) printed inside of the passport. This MRZ must be read off the passport and then provided to the RFID chip as a PIN code to gain access. It also uses this information to base encryption between the RFID tag and RFID reader.
  Random ID (RID) which presents a new random ID each time the passport is read. It maintains the same ID during a communication session, but after the session is complete it will generate a new one. This was implemented to prevent using the ID of the RFID device as a tracking means.
VeriChip, the first FDA approved human implantable RFID chip using the ISO 11784 134 KHz standard which is a variant of the LF standard.
Printable RFID stickers using with LF or HF RFID embedded chips, which leads us to…

## Slide 5
Notes: Google Places window sticker
Sticker contains a 13.56 MHz ~1 meter RFID chip embedded in it
Each tag is encoded with an ID number that communicates with NFC-enabled phones to display the appropriate Place Page for that business.
Customers bring their phone within the 1m range of the sticker and it auto loads the Places page on their device allowing them to “check in,” get location details, receive coupons, etc.

## Slide 6: What then is NFC?
Near Field Communication
  Technical Details
    NFCIP-1 & NFCIP-2 ~ ISO 180921 & 21481
    NFCIP-1
      ISO 14443
        13.56 MHz with a range of 1 meter
        Identification Cards
      ISO 15693
        13.56 MHz with a range of 1.5 meters
        Vicinity Cards (not Proximity Cards)
    NFCIP-2
      NFCIP-1 + communication mode selection mechanism designed to not disturb any ongoing communication at 13.56 MHz
Notes: NFCIP = Near Field Communication Interface and Protocol
NFC itself is a subset of the RFID protocol but is actually a collection of RFID protocols with additional intent information along with usage standards.
The 13.56 MHz HF range is currently the most commonly used thanks to the benefit in range and power capabilities. The cheap production costs, increased range, and expanded memory capacity provide for a beneficial platform for mass production.

## Slide 7: What does NFC mean to me?
Primarily intended for use in mobile devices.
Payment Systems
  Used in Europe and Asian countries currently
  AT&T, T-Mobile, and Verizon joined together (Nov 2010) to create a single standard for NFC payments in the USA
Information Systems
  Google Places stickers
P2P Systems (Phone 2 Phone)
  Android 2.3.3 (Feb 2011) added the ability to not only read NFC tags but the ability to broadcast as an NFC device. This new capability allows phones to share data within short ranges of each other.
Notes: Payment systems has been the primary driving force behind the NFC standards. The intent is to provide an extremely simplistic method of purchasing by use of a mobile device. By passing your device over an NFC payment system they begin communication allowing the user to then authenticate the purchase from their device.
Japan was one of the first countries to begin using NFC originally in vending machines. The technology has grown and is much more widely used in many Asian and European countries now.
USA phone carriers are willing to work together on this technology because they get a cut of every transaction as the purchasing gateway.
Currently in the USA only the Nexus S smartphone contains the technology to do NFC however numerous phones were announced in early Feb with intent to deliver soon.
Google along with the other USA carriers plan to back the technology heavily so acceptance should begin soon and ramp up quickly since they would see a financial benefit from this technology.
There are rumors Apple will support NFC in the next generation iPhone/iPod/iPad but not solid confirmation has been made or if their implementation would work with the other systems. Job postings for NFC knowledgeable positions have been seen over the last several months from Apple lending to these rumors.
With the newest release of Android 2.3.3 this month, Google has added P2P capabilities to the existing SDK. With these available technologies developers will be able to create applications that can communicate directly between phones without the need of other more complex processes like Bluetooth pairing or WiFi AdHoc. This should provide for new systems that provide rapid data sharing with minimal effort.
These libraries also allow a phone to behave as if it is an NFC tag as well, responding to NFC requests from other mobile devices.
Depending on the types of chips used for various NFC devices the available capabilities also provides the means to rewrite the information inside of writeable NFC tags.

## Slide 8: RFID Security Threats
Notes: Application Layer
  Spoofing – Due to the fact that a lot of RFID devices function on standard protocols and provide basic ID data un-encrypted it becomes extremely easy to acquire an RFIDs ID value and then use it either via writing the value to another ID card or RFID cloning techniques. This permits a person to then masquerade as the person whose ID they've spoofed. Prevention: Require a minimum of two-factor authentication.
  Replay – An attacker only has to know the format of which to transmit an ID to the reader(s) in order to perform a replay attack. They begin transmitting previously captured data over and over again in attempts to overwhelm the reader, the network, and the backend system. This can be viewed as a Denial of Service (DoS) or Distributed DoS (DDoS) by attacking multiple readers at the same time. The resulting heavy load can then prevent valid readers not being attacked from not passing valid data along if the network or the backend cannot handle the load any longer. Prevention: Detecting the same ID being connected over and over again can allow blocking of those connections. If the IDs are random more advanced detection techniques are required.
  Tracking – This is an attack on the RFID holder themselves and no the RFID system. Because most RFID tags return the same ID even if its encrypted, that unique value can be used to track the owner of the RFID tag. This can be used to monitor times they enter or leave specific locations and which locations they visit. Prevention: Train personal to keep their RFID tags inside of casings that prevent reading them at a distance.
  Desynchronization – Through a variety of means desynchronization is the process of making a RFIDs ID desynchronized with the backend systems it is linked with. This can be done by attacking the backend or sending a write command to a RFID tag. Prevention: Train personal to keep their RFID tags inside of casings that prevent writing them at a distance. Securing the backend from manipulation.
  Virus – Since most systems are fairly trusting of the data coming off of an RFID tag it could be possible to encode malicious content into the values of an RFID tag. An example would be replacing a tags values with a SQL Injection attack that would allow the inserting of code into SQL tables, executing commands against the, deleting data, or inserting data. Prevention: Backend must filter and protect incoming data from harming the system.
Communication Layer
  Collision – Because of the limitation of most readers or RFID tags to only engage one device at a time it makes it possible to then flood a device preventing roper or reliable communication. Bogus communication data is flooded at a device colliding with the correct data causing it to be ignored. The more simultaneous signals being sent the more likely you are to collide with valid packets knocking them out. This in essence is a Denial of Service (DoS) type attack against RFID.
Physical Layer
  RF Eavesdropping – Because the spectrums for devices are known an attacker only needs to just listen for broadcasted signals to find them. Most implementations use known components so modulation schemes are also typically known. Also due to the power and price limitation on most RFID tags advanced protection schemes are either unavailable or impossible.
  Jamming – As with eavesdropping, because most information is known about how devices work and what frequencies they operate on it becomes easy to broadcast similar signals to jam the signal from being received. By jamming RFID signals one can prevent the tag or reader from properly receiving the correct signals they should get.
  Cloning – Since the information sent by RFID in most cases stays the same from use to use cloning is an effective threat against these devices. Due to the ease of eavesdropping a signal can be replicated and played back in essence cloning a device via RF equipment. This however is only a direct playback and does not provide knowledge of what exactly is in the signal.

## Slide 9: What we propose
Attempt to prove the ability to perform malicious attacks with NFC by simulating:
  Planting rogue NFC tags
  Re-writing existing tags to incorporate malicious payload/intent
Develop a framework to provide IDS/IPS
  OS integration, Middle-ware, or Developer implementations
  Detect or detect & prevent attacks
NFC IDS/IPS App
Spoofing, Relay, Malware, Injection, XSS, fuzzing, etc.
Notes: With all of the potential security concerns that surround NFC there must be a way to detect or even possibly prevent these attacks from occurring. With all the information that has been covered thus far and with this being an up and coming technology, it is just a matter of time before the security of NFC becomes a major concern. In this research we intend to prove the ability to perform malicious acts by simulating the planting rogue NFC tags or re-writing existing ones to contain malicious content to be triggered either in an SQL Injection, XSS, buffer overflow, etc type of attack against the mobile device. Once proven we intend to used a proposed framework to develop a capability to provide IDS/IPS like behavior to either just detect or detect & prevent these types of attacks. We will attempt to research where this technology could be best suited which includes either at the OS integration, Middle-ware application, or Developer implementation.

## Slide 10: Approach
Develop a “proof-of-concept” framework
Identify
Discover possible threats or vectors of attack
Devise
Develop a signature to detect threat
Implement
Proxy NFC traffic and sniff/block matching signatures
11010110malware10110100
11010110malware10110100
11010110malware10110100
!! X
Notes: The framework to “sniff or sniff & intercept” malicious signatures in NFC communications involves three categories, Identify, Devise, and Implement.
Identify: This is the beginning phase of the framework which is centered around discovering the various vectors of attack. Some of these attacks were discussed on previous slides but can include SQL injection, XSS, replay, or even a piece of malicious payload such as a virus, Trojan, or worm.
Devise: The second phase of the framework is about devising a method of detection or signature that can match a particular piece of data. This data could be a piece of meta data, fraction of a payload or a string of binary. If an exploit was created and implanted on a NFC tag such as a sticker and perhaps placed on top of the up and coming Google NFC stickers it could be attempting to take advantage of a vulnerability on the mobile device and opening it to further attack. A signature could be devised to detect known exploit code.
Implement: the third and final phase of the framework is applying the newly devised signature into the mechanism that performs IDS/IPS. As the NFC data is transmitted, it is sniffed to detect data against all possible devised signatures and raise an alarm or even discard and prevent the data from being received.

## Slide 11: References
Radio Frequency IDentification (RFID), 2010, Leith Tussing
RFID Security, 2010, Abirami Poonkundran, Leith Tussing, Jose Velez, Steve Grimes, Sharif Hassan
Android Developers SDK
  http://developer.android.com/sdk/android-2.3.3.html
  http://developer.android.com/reference/android/nfc/package-summary.html
Wikipedia
  http://en.wikipedia.org/wiki/Near_field_communication
  http://en.wikipedia.org/wiki/ISO/IEC_18092
  http://en.wikipedia.org/wiki/ISO/IEC_21481

## Slide 12
Attacks on NFC mobile phones demonstrated, 2008, Dancho Danchev
  http://www.zdnet.com/blog/security/attacks-on-nfc-mobile-phones-demonstrated/1210
Attacking NFC Mobile Phones, 2008, Collin Mulliner
  http://www.mulliner.org/nfc/feed/collin_mulliner_eusecwest08_attacking_nfc_phones.pdf
Security in Near Field Communication (NFC), 2006, Ernst Haselsteiner and Klemens Breitfuß
  http://events.iaik.tugraz.at/RFIDSec06/Program/papers/002%20-%20Security%20in%20NFC.pdf
Practical NFC Peer-to-Peer Relay Attack using Mobile Phones, 2010, Lishoy Francis, Gerhard Hancke, Keith Mayes, and Konstantinos Markantonakis
  http://eprint.iacr.org/2010/228.pdf