## Slide 1: Security Vulnerabilities in Cognitive Radio Networks and Counter Measures
Muhammad Faisal Amjad
CAP - 6135

## Slide 2: Aim
To investigate security vulnerabilities of Cognitive Radio Networks with special emphasis on Denial of Service attacks, their existing counter measures, and propose alternate solution(s).
Acknowledgement: References at the end are the sources of various definitions, concepts, figures and data used in this presentation.

## Slide 3: Sequence
Background
Definition of Cognitive Radio (CR)
Classification of Cognitive Radio
Cognitive Radio Architecture
Security Vulnerabilities of CR Networks
Outline Plan of Study & Outcomes

## Slide 4: Background
Spectrum utilization depends on time and space
Most of the radio frequency spectrum is utilized inefficiently [1]
  cellular network bands vs. amateur radio bands
Fixed spectrum allocation naturally leads to wastage of already scarce radio resources
Efficiency can be improved by allowing unlicensed users to exploit spectrum whenever it would not cause interference to licensed users
This gave rise to the paradigm of Cognitive Radio (CR) in which CR devices also called the Secondary Users, opportunistically use the frequency band(s) whenever the incumbent / Licensed Primary Users do not.

## Slide 5: Definition of Cognitive Radio
The idea of cognitive radio was first presented officially by Joseph Mitola III [2], who described the term as
“The point in which wireless PDAs and the related networks are sufficiently computationally intelligent about radio resources and related computer-to-computer communications to detect user communications needs as a function of context, and to provide radio resources and wireless services most appropriate to those needs”.

## Slide 6: Definition of Cognitive Radio
FCC has defined a cognitive radio [3] as
“A radio that can change its transmitter parameters based on interaction with the environment in which it operates.”

## Slide 7: Cognitive Radio Cycle [4]

## Slide 8: Classification of Cognitive Radio [5]
Based on the number of parameters
  Full Cognitive Radio (a.k.a Mitola Radio)
  Spectrum Sensing Cognitive Radio
    IEEE 802.22 WRAN is the first standard based on CR and the working group is aiming to utilize white spaces in the TV bands.
Based on the parts of spectrum available for CR
  Licensed Band Cognitive Radio
  Unlicensed Band Cognitive Radio

## Slide 9: Cognitive Radio Architecture [6]

## Slide 10
IEEE 802.22 CR Network Architecture [7]
TV transmitters
WRAN
Base Station
Wireless
microphones
Wireless
microphones
WRAN
Base Station
: CPE (Consumer Premise Equipment)
: WRAN Base Station
Typical ~33km
Max. 100km
Incumbent services:
TV broadcast services
Part 74 devices (wireless microphones)

## Slide 11: Approaches to Spectrum Sensing in 802.22
Centralized servers provide information on available channels in the area of Base Station / Access Point (AP)
Base station resorts to local spectrum sensing only, where it would independently decide which channels are available
A combination of above

## Slide 12: Spectrum Usage Scenario for a Secondary User
  Periodically search for spectrum “white spaces” (i.e., fallow bands) to transmit/receive data
  When a primary user is detected in its spectrum band
    Immediately vacate that band and switch to a vacant one
      “vertical spectrum sharing”
  When another secondary user is detected in its spectrum band
    When there are no better spectrum opportunities, it may choose to share the band with the detected secondary user
      “horizontal spectrum sharing”

## Slide 13: A Taxonomy of CR Security Vulnerabilities [7]
CR network
security threats
Radio software
security threats
Spectrum access
-
related security threats
Threats to incumbent
coexistence mechanisms
Threats to self
-
coexistence mechanisms
Security threats to the
software download process
Sensory manipulation
:
Primary user emulation
Geospatial manipulation
Chaff point attack
Spam point bias attack
Tx false
/
spurious inter
-
cell
beacons
(
control messages
)
Exploit
/
obstruct inter
-
cell
spectrum sharing processes
Unauthorized policy changes
Tampering w
/CR reasoners
(
e
.
g
.
,
System Strategy Reasoner
&
Policy Reasoner
)
IP theft
Software tampering
Injection of false
/ forged
policies
Injection of false
/
forged
SW updates
Injection of malicious SW
(
viruses
)

## Slide 14: Primary User Emulation Attack [7]

## Slide 15: Spectrum Sensing Data Falsification Attack [7]

## Slide 16: The Disruptive Effects of Primary User Emulation Attacks [7]
Malicious PUE attacks
Selfish PUE attacks

## Slide 17: Outline Plan of Study & Outcomes
A study of the state of the art in defense against DoS attacks in CR Networks.
Find shortcomings and / or suggest improvements in existing solutions
Conduct simulations whenever required for any proof of concept(s)
Final outcome of this project will ideally be a research paper publication in a scientific conference

## Slide 18
?

## Slide 19: References
[1]. IEEE Spectrum: The End of Spectrum Scarcity, http://www.spectrum.ieee.org/mar04/3811
[2]. Dr. Joseph Mitola III, Cognitive Radio An Integrated Agent Architecture for Software Defined Radio Dissertation, p. 1,para 1.1, Royal Institute of Technology, May 8, 2000.
[3]. B. Fette, “Introduction to Cognitive Radio,” SDR Forum Technical Conference 2005, Nov. 14-17, Orange County, CA.
[4]. University of Maryland, Signals & Information Group, http://www.cspl.umd.edu/sig/research/
[5]. J. Mitola III and G. Q. Maguire, Jr., "Cognitive radio: making software radios more personal," IEEE Personal Communications Magazine, vol. 6, nr. 4, pp. 13-18, Aug. 1999
[6]. Broadband Wireless Networking Lab, GA Institute of Technology, http://www.ece.gatech.edu/research/labs/bwn/CR/
[7]. “Cognitive radio communications and networks: principles and practice”, Alexander M. Wyglinski, Maziar Nekovee, Y. Thomas Hou, Elsevier December 2009.